|  | REQUEST FOR PROPOSALS (RFP) Department of Administration County of Dane, Wisconsin |
| --- | --- |
| COUNTY AGENCY | Alliant Energy Center |
| RFP NUMBER | #115073 |
| RFP TITLE | Alliant Energy Center Exposition Hall Audio Equipment Upgrade |
| PURPOSE | The purpose of this document is to provide interested parties with information to enable them to prepare and submit a proposal for the Alliant Energy Center Exposition Hall audio equipment upgrade. |
| DEADLINE FOR RFP SUBMISSIONS | 2:00 P.M. Central Time July 8, 2015 LATE, FAXED, ELECTRONIC MAIL OR UNSIGNED PROPOSALS WILL BE REJECTED |
| SUBMIT RFP TO THIS ADDRESS | DANE COUNTY PURCHASING DIVISION ROOM 425 CITY- COUNTY BUILDING 210 MARTIN LUTHER KING JR BLVD MADISON, WI 53703-3345 |
| VENDOR CONFERENCE | Wednesday, June 17, 2015 at 10:30 a.m. Alliant Energy Center Administration Conference Room 1919 Alliant Energy Center Way, Madison, WI 53713 |
| SPECIAL INSTRUCTIONS | Label the lower left corner of your sealed submittal package with the RFP number Place the Signature Affidavit as the first page of your proposal Submit one original and ( 3 ) copies of your technical proposal Submit one original and ( 1 ) copies of your cost proposal Submit one complete electronic copy in Microsoft Word or PDF format burned to a CD, DVD or flash drive. |
| DIRECT ALL INQUIRES TO | NAME | Carolyn A. Ninedorf |
|  | TITLE | Purchasing Agent |
|  | PHONE # | 608/266-4966 |
|  | FAX # | 608/266-4425 |
|  | EMAIL | Ninedorf.carolyn@countyofdane.com |
|  | WEB SITE | www.danepurchasing.com |
| DATE RFP ISSUED: June 8, 2015 |

RFP BLANK REVISED 9/12

TABLE OF CONTENTS

| 1.0 | GENERAL INFORMATION |
| --- | --- |
|  | 1.1 | Introduction |
|  | 1.2 | Scope |
|  | 1.3 | Definitions |
|  | 1.4 | Clarification of the specifications |
|  | 1.5 | Addendums and or revisions |
|  | 1.6 | Calendar of events |
|  | 1.7 | Vendor conference |
|  | 1.8 | Contract term and funding |
|  | 1.9 | Reasonable accommodations |
| 2.0 | PREPARING AND SUBMITTING A PROPOSAL |
|  | 2.1 | General instructions |
|  | 2.2 | Proprietary information |
|  | 2.3 | Incurring costs |
|  | 2.4 | Vendor registration |
|  | 2.5 | Submittal instructions |
|  | 2.6 | Required copies |
|  | 2.7 | Proposal organization and format |
|  | 2.8 | Multiple proposals |
|  | 2.9 | Oral presentations and site visits |
|  | 2.10 | Demonstrations |
| 3.0 | PROPOSAL SELECTION AND AWARD PROCESS |
|  | 3.1 | Preliminary evaluation |
|  | 3.2 | Proposal scoring |
|  | 3.3 | Right to reject proposals |
|  | 3.4 | Evaluation criteria |
|  | 3.5 | Award and final offers |
|  | 3.6 | Notification of intent to Award |
| 4.0 | GENERAL PROPOSAL REQUIREMENTS |
|  | 4.1 | Introduction |
|  | 4.2 | Organization capabilities |
|  | 4.3 | Staff qualifications |
|  | 4.4 | Proposer references |
|  | 4.5 | Mandatory requirements |
| 5.0 | TECHNICAL REQUIREMENTS |
|  | 5.1 | Overview of technical requirements |
| 6.0 | COST PROPOSAL |
|  | 6.1 | General instructions on submitting cost proposals |
|  | 6.2 | Format for submitting cost proposals |
|  | 6.3 | Fixed Price Period |
| 7.0 | SPECIAL CONTRACT TERMS AND CONDITIONS |
|  | 7.1 | Living wage requirement |
|  | 7.2 | Domestic Partner Equal Benefits Requirement |
|  | 7.3 | Local Purchasing Ordinance |
|  | 7.4 | Dane County Sustainability Principles |

| 8.0 | REQUIRED FORMS |
| --- | --- |
|  | ATTACHMENTS |
|  |  | A. | Signature Affidavit |
|  |  | B | Vendor Registration Certification |
|  |  | C. | Reference Data Sheet |
|  |  | D. | Designation of Confidential and Proprietary Information |
|  |  | E. | Fair Labor Practices Certification |
|  |  | F. | Vendor Data Sheet |
|  |  | G. | Cost /Financial Proposal |
| 9.0 | STANDARD TERMS & CONDITIONS |
| 10.0 | AUDIO-VISUAL SYSTEMS 27 40 00 - 3 |
| 11.0 | COMMON WORK RESULTS FOR COMMUNICATIONS SYSTEMS 27 05 00 - 3 |

| 1.0 | GENERAL INFORMATION |
| --- | --- |
|  | 1.1 | Introduction |
|  |  | The purpose of this document is to provide interested parties with information to enable them to prepare and submit a proposal for Alliant Energy Center Audio Equipment Upgrade. The County intends to use the results of this process to award a contract(s) or issuance of purchase order for the product(s) and or services(s) stated above. The contract resulting from this RFP will be administered by Alliant Energy Center (AEC) Facility Management The contract administrator will be Mark Clarke. This Request for Proposal (RFP) is issued on behalf of Dane County by the Purchasing Division, which is the sole point of contact for the County during the procurement process. |
|  | 1.2 | Scope of the Project |
|  |  | 1.2.1 | AEC is seeking a qualified AV Integrator to provide installation services to upgrade or modify existing AV systems at AEC in the Exhibition Hall building. The goals of the upgrade are: Provide state-of-the-art digital audio systems for hall A-D, meeting rooms, common area, encompassing roughly 150,000 square feet. These room quantities should be reconfirmed with the County during the pre-bid walk-thru. Because all rooms have existing systems that use primarily analog transport with associated cables and connectors, the primary or first goal is to permit digital transport and control by replacing older devices with current digital interfaces, cables and connectors and inserting new digital signal processors (DSPs) and user interfaces. The primary goal is to permit staff to switch and route audio signals between various venues using the existing Ethernet network switches and existing speakers and wire with the introduction of new DSPs and touchscreen user interfaces to provide control. There are four (4) AV rooms having multiple existing inputs and outputs to various venues. Each AV room has existing wiring, mixers, amplifiers, inputs from wall jacks and outputs to existing amplifiers and speakers. The intent is to remove the existing audio mixers and replace them with DSPs, control processors and touch panel displays to permit easy, intuitive routing of inputs and outputs while leaving in place all the other parts of the system including XLR inputs, amplifiers, speakers and wiring. CobraNet protocol will be used due to its network compatibility, stability and ease of use. The scope includes tuning and balancing the system in every venue after the new head-end equipment is installed. There are multiple venues therefore this is a major aspect of the project. Consult closely with owner to relocate or adjust existing equipment to create room for new touch panel display within racks. |
|  |  | 1.2.2 | This plan consists of technical requirements outlined in narrative form in section 5 of this RFP combined with one-line documents attached separately. Together the narrative and one-line constitute the requirements that must be met. Installation crews may have to work around existing event schedules and work locations will be coordinated with AEC staff to fit in the event schedule. |
|  |  | 1.2.3 | The AV system needs to do the following: Allow for clear voice communication for public address, presentations, lectures, group meeting, large public assembly functions Utilize the existing speakers and wiring Utilize the existing Ethernet network for audio transport between various venues and buildings Utilize all other existing equipment to the greatest extent possible Permit switching and routing of audio signals from any of four AV rooms to any other AV room and out to any venue. Any audio input from any location should be able to be routed to any other venue from any of four control points (AV rooms). |
|  |  | 1.2.4 | Current Operations using analog connections will need to continue uninterrupted during the AV system upgrade until the time that new DSPs and processors are installed. Integrator may need to alter work schedules, work after hours, work partial days or in other ways accommodate the event schedule. |
|  | 1.3 | Definitions |
|  |  | The following definitions are used throughout the RFP. |
|  |  | County means Dane County |
|  |  | County Agency means Department /Division utilizing the service or product AEC mean Alliant Energy Center |
|  |  | Proposer/vendor means a firm submitting a proposal in response to this RFP. |
|  |  | Contractor means proposer awarded the contract. |

|  | 1.4 | Clarification of the specifications |
| --- | --- | --- |
|  |  | All inquiries concerning this RFP must be directed to the person indicated on the cover page of the RFP Document. (electronic mail is the preferred method) Any questions concerning this RFP must be submitted in writing by mail, fax or e-mail on or before the stated date on the Calendar of Events (see Section 1.6) Proposers are expected to raise any questions, exceptions, or additions they have concerning the RFP document at this point in the RFP process. If a proposer discovers any significant ambiguity, error, conflict, discrepancy, omission, or other deficiency in this RFP, the proposer should immediately notify the contact person of such error and request modification or clarification of the RFP document. Mailing Address: Dane County Purchasing Division Room 425 City-County Bldg. 210 Martin Luther King Jr. Blvd Madison, WI 53703-3345 |
|  |  | Proposers are prohibited from communicating directly with any employee of Dane County, except as described herein. No County employee or representative other than those individuals listed as County contacts in this RFP is authorized to provide any information or respond to any question or inquiry concerning this RFP. |
|  | 1.5 | Addendums and/or Revisions |
|  |  | In the event that it becomes necessary to provide additional clarifying data or information, or to revise any part of this RFP, revisions/amendments and/or supplements will be posted on the Purchasing Division web site at www.danepurchasing.com It shall be the responsibility of the proposers to regularly monitor the Purchasing Division web site for any such postings. Proposers must acknowledge the receipt / review of any addendum(s) at the bottom of the RFP Cover Page /Signature Affidavit. Each proposal shall stipulate that it is predicated upon the terms and conditions of this RFP and any supplements or revisions thereof. |
|  | 1.6 | Calendar of Events |
|  |  | Listed below are specific and estimated dates and times of actions related to this RFP. The actions with specific dates must be completed as indicated unless otherwise changed by the County. In the event that the County finds it necessary to change any of the specific dates and times in the calendar of events listed below, it will do so by issuing a supplement to this RFP and posting such supplement on the Dane County web site at www.danepurchasing.com . There may or may not be a formal notification issued for changes in the estimated dates and times. |
| DATE | EVENT |
| June 8, 2015 | Date of issue of the RFP |
| June 17, 2015 10:30 a.m. | Vendor conference |
| June 23, 2015 | Last day for submitting written inquiries (2:00 p.m. Central Time) |
| June 24, 2015 | Supplements or revisions to the RFP posted on the Purchasing Division web site at www.danepurchasing.com |
| July 8, 2015 | Proposals due from vendors |
| July 2015 | Oral presentation by invited vendors, if needed |
| Late July 2015 | Notification of intent to award sent to vendors |
| September 18, 2015 | Contract completion date |
|  | 1.7 | Vendor Conference |
|  |  | A mandatory vendor conference will be held to respond to written questions and to provide any needed additional instruction to vendors on the submission of proposals. All vendors who intend to respond to the RFP shall to attend the vendor conference. If a vendor fails to attend the conference and submits a proposal, the proposal will be rejected. Date: Wednesday, June 17th 2015 Time: 10:30 a.m. Location: Alliant Energy Center, 1919 Alliant Energy Center Way. |
|  | 1.8 | Contract Term and Funding |
|  |  | The contract shall be effective on the date indicated on the purchase order or the contract execution date and shall run though September 30, 2015. |
|  | 1.9 | Reasonable Accommodations |
|  |  | The County will provide reasonable accommodations, including the provision of informational material in an alternative format, for qualified individuals with disabilities upon request. If you need accommodations at a proposal opening/vendor conference, contact the Purchasing Division at (608) 266-4131 (voice) or Wisconsin Relay (711). |
| 2.0 | PREPARING AND SUBMITTING A PROPOSAL |
|  | 2.1 | General Instructions |
|  |  | The evaluation and selection of a contractor and the contract will be based on the information submitted in the proposal plus references and any required on-site visits or oral interview presentations. Failure to respond to each of the requirements in the RFP may be the basis for rejecting a response. |
|  |  | Elaborate proposals (e.g. expensive artwork) beyond that sufficient to present a complete and effective proposal, are not necessary or desired. |
|  | 2.2 | Proprietary Information |
|  |  | All restrictions on the use of data contained within a proposal and all confidential information must be clearly stated on the attached “Designation of Confidential and Proprietary Information” form. Proprietary information submitted in a proposal, or in response to the RFP, will be handled in accordance with the applicable Wisconsin State Statute(s). |
|  |  | To the extent permitted by law, it is the intention of Dane County to withhold the contents of the proposal from public view until such times as competitive or bargaining reasons no longer require non-disclosure, in the opinion of Dane County. At that time, all proposals will be available for review in accordance with the Wisconsin Open Records Law. |
|  | 2.3 | Incurring Costs |
|  |  | Dane County is not liable for any cost incurred by proposers in replying to this RFP. |
|  | 2.4 | Vendor Registration |
|  |  | All proposers wishing to submit a proposal must be a paid registered vendor with Dane County. Prior to the RFP opening, you can complete a registration form online by visiting our web site at www.danepurchasing.com, or you can obtain a Vendor Registration Form by calling 608.266.4131. Your completed Vendor Registration Form and Registration Fee must be received for your bid to be considered for an award. |
|  | 2.5 | Submittal Instructions |
|  |  | Proposals must be received in by the County Purchasing Division by the specified time stated on the cover page. All proposals must be time-stamped in by the Purchasing Division by the stated time. Proposals not so stamped will not be accepted. Proposals received in response to this solicitation will not be returned to the proposers. All proposals must be packaged, sealed and show the following information on the outside of the package: Proposer’s name and address Request for proposal title Request for proposal number Proposal due date |

|  | 2.6 | Required Copies |
| --- | --- | --- |
|  |  | Proposers must submit an original and the required number of copies of all materials required for acceptance as instructed on the cover page of the RFP (Special Instructions). All hard copies of the proposal must be on 8.5”x11” individually securely bound. In addition, proposers must submit one complete electronic copy in Microsoft Word or PDF format burned to a CD, DVD or flash drive. |
|  | 2.7 | Proposal Organization and Format |
|  |  | Proposals should be organized and presented in the order and by the number assigned in the RFP. Proposals must be organized with the following headings and subheadings. Each heading and subheading should be separated by tabs or otherwise clearly marked. The RFP sections which should be submitted or responded to are: |
|  | Introduction (See Section 4 of this RFP) |
|  | Response to general requirements (See Section 4 of this RFP) |
|  | Organizational qualifications |
|  | Staff qualifications and Facilities |
|  | References |
|  | Response to technical requirements (See Section 5 of this RFP) |
|  | Cost proposal (See Section 6 of this RFP) |
|  | Required forms (See Section 8 of this RFP) |
|  | Attachment A | Signature Affidavit |
|  | Attachment B | Vendor Registration Certification |
|  | Attachment C | Reference Data Sheet |
|  | Attachment D | Designation of Confidential and Proprietary Information |
|  | Attachment E | Fair Labor Practices Certification |
|  | Attachment F | Vendor Data Sheet |
|  | Attachment G | Cost Summary Page |
|  | Appendices (Additional Information the proposer submits) |
|  | 2.8 | Multiple Proposals |
|  |  | Multiple proposals from a vendor will be permissible, however each proposal must conform fully to the requirements for proposal submission. Each such proposal must be separately submitted and labeled as Proposal #1, Proposal #2, etc. |
|  | 2.9 | Oral Presentations and Site Visits |
|  |  | Top ranked selected proposers may be required to make oral interview presentations and/or site visits to supplement their proposals, if requested by the County. The County will make every reasonable attempt to schedule each presentation at a time and location that is agreeable to the proposer. Failure of a proposer to conduct a presentation to the County on the date scheduled may result in rejection of the vendor’s proposal. |

| 3.0 | PROPOSAL SELECTION AND AWARD PROCESS |
| --- | --- |
|  | 3.1 | Preliminary Evaluation |
|  |  | The proposals will first be reviewed to determine if requirements in Section 2.0 are met, and if additional mandatory requirements are met. (see Section 4.0). Failure to meet mandatory requirements will result in the proposal being rejected. In the event that all vendors do not meet one or more of the mandatory requirements, the County reserves the right to continue the evaluation of the proposals and to select the proposal which most closely meets the requirements specified in this RFP. |
|  | 3.2 | Proposal Scoring |
|  |  | Accepted proposals will be reviewed by an evaluation team and scored against the stated criteria. This scoring will determine the ranking of vendors based upon their written proposals. If the team determines that it is in the best interest of the County to require oral presentations, the highest ranking vendors will be invited to make such presentations. Those vendors that participate in the interview process will then be scored, and the final ranking will be made based upon those scores. |
|  | 3.3 | Right to Reject Proposals and Negotiate Contract Terms |
|  |  | The County reserves the right to reject any and all proposals and to negotiate the terms of the contract, including the award amount, with the selected proposer prior to entering into a contract. If contract negotiations cannot be concluded successfully with the highest scoring proposer, the County may negotiate a contract with the next highest scoring proposer. |

|  | 3.4 | Evaluation Criteria |
| --- | --- | --- |
|  |  | The proposals will be scored using the following criteria: |
|  | Description |  | Percent |
| 1. | General requirements |  | 40 |
|  | a. | Organization capabilities and staff qualifications (Sections 4.2 & 4.3) |  |  |
| 2. | Technical requirements |  | 30 |
|  | a. | Bill of materials, detailed one line diagram, timeline and project approach (Section 5) |  |  |
| 3. | Cost |  | 30 |
|  | TOTAL | 100 |
|  | 3.5 | Award and Final Offers |
|  |  | The award will be granted in one of two ways. The award may be granted to the highest scoring responsive and responsible proposer. Alternatively, the highest scoring proposer or proposers may be requested to submit final and best offers. If final and best offers are requested, they will be evaluated against the stated criteria, scored and ranked. The award will then be granted to the highest scoring proposer. |
|  | 3.6 | Notification of Intent to Award |
|  |  | As a courtesy, the County may send a notification of award memo to responding vendors at the time of the award. |
| 4.0 | GENERAL PROPOSAL REQUIREMENTS |
|  | 4.1 | Introduction Provide a one page letter of interest in the project. Include a brief description of company history, mission, expertise and availability. |
|  | 4.2 | Organization Capabilities |
|  |  | Describe the firm’s experience and capabilities in providing similar services to those required. Be specific and identify projects, dates, and results. Provide no fewer than three and no more than six similar projects. If your company belongs to any industry trade groups or is certified by trade groups or manufacturers, list the certifications. |
|  | 4.3 | Staff Qualifications |
|  |  | Provide resumes describing the educational and work experiences for each of the key staff who would be assigned to the project. Provide industry certifications from InfoComm, BICSI or other trade organizations. Provide manufacturer certifications (not merely training courses but actual certifications recognized by the manufacturer or industry). It is required that the bidder have at least one Infocomm CTS-I or CTS-D assigned to this project. Indicate AV system control programming capabilities and experience. |
|  | 4.4 | Proposer References |
|  |  | Proposers must include in their RFPs a list of organizations, including points of contact (name, address, and telephone number), which can be used as references for work performed in the area of service required. Selected organizations may be contacted to determine the quality of work performed and personnel assigned to the project. |
|  | 4.5 | Mandatory Requirements |
|  |  | The following general requirements are mandatory and must be complied with. Provide a narrative describing how the firm meets the following requirements: |
|  |  | 4.5.1 | Staff having CTS-I or CTS-D certification |
|  |  | 4.5.2 | Be certified by the manufacturer for the control system products to be installed. |
| 5.0 | TECHNICAL REQUIREMENTS |
|  | 5.1 | Overview of technical requirements |
|  |  | The requirements noted below are of a summary nature. For specific requirements regarding products and installation, refer to the accompanying drawings and specification 27 40 00- Appendix 1. Provide a bill of materials (with line item costs, if possible) and a detailed one line diagram, as well as an overview of the timeline and project approach that the firm will use for the project. |
|  |  | 5.1.1 | AV Room #1 - Main Electrical Room Remove existing audio mixer(s) Provide new audio DSP with input/output cards Provide new control system Provide PoE injectors as required and coordinate with owner to utilize existing Ethernet infrastructure Provide new 10” touch screen user interface Provide custom rack panel with cutout for touch screen Patch cables, connectors, hardware, programming and installation Testing, balancing and tuning of speakers in Exhibit Hall A, B, C, D and Lobby |
|  |  | 5.1.2 | AV Room #2 – Area F, Lake Room, Upper Level Meeting Rooms Remove existing audio mixer(s) Provide new audio DSP with input/output cards Provide new control system Provide PoE injectors as required and coordinate with owner to utilize existing Ethernet infrastructure Provide new 10” touch screen user interface Provide custom rack panel with cutout for touch screen Patch cables, connectors, hardware, programming and installation Testing, balancing and tuning of speakers in Upper Level Meeting Rooms L, MO, WI, WA, KE and B. |
|  |  | 5.1.3 | AV Room #3 – Area E, Mendota 4 Sound Room, Rooms M1-M4 Remove existing audio mixer(s) Provide new audio DSP with input/output cards Provide new control system Provide PoE injectors as required and coordinate with owner to utilize existing Ethernet infrastructure Provide new 10” touch screen user interface Provide custom rack panel with cutout for touch screen Patch cables, connectors, hardware, programming and installation Testing, balancing and tuning of speakers in Rooms M1-M4 |
|  |  | 5.1.1 | AV Room #4 – Area E, Mendota 8 Sound Room, Rooms M5-M8 with Atrium Remove existing audio mixer(s) Provide new audio DSP with input/output cards Provide new control system Provide PoE injectors as required and coordinate with owner to utilize existing Ethernet infrastructure Provide new 10” touch screen user interface Provide custom rack panel with cutout for touch screen Patch cables, connectors, hardware, programming and installation Testing, balancing and tuning of speakers in Rooms M5-M5 and Atrium |
|  | 5.2 | Overview of technical requirements – Alternate #1 |
|  |  | 5.2.1 | Replace Existing XLR Faceplate and Jack with New Provide price to remove and replace one existing faceplate and XLR connection in Main Exibit Hall or Meeting Rooms with new XLR connection and faceplate (total quantity may reach 70 locations) Unsolder existing XLR connectors and replace with new XLR connector. Do not replace phono TRS connector and do not replace any wiring in the walls – only XLR connector. Some XLR connectors are riveted and my need to be drilled out. Retain use of existing wall faceplates that are etched and labeled. Faceplates in floor boxes should be replaced with like materials (stainless steel and gasketed if required). |
|  |  | 5.2.2 | Rotate existing AV racks #3 and #4 180 degrees in place Provide price to adjust cables, equipment and AV racks so that AV rack can be rotated in place 180 degrees in order to face in the logical direction – towards the entry door. Price should include labor for two AV racks, AV #3 and AV #4 only as a consolidated price to rotate both racks. |
| 6.0 | COST PROPOSAL |
|  | 6.1 | General Instructions on Submitting Cost Proposals |
|  |  | Proposers must submit an original and the required number of copies of the cost proposal as instructed on the cover page of the RFP (Special Instructions). Cost proposal should be submitted in a separate envelope labeled Cost Proposal with the written proposal. (Refer to Cost Proposal Form.) The proposal will be scored using a standard quantitative calculation where the most cost criteria points will be awarded to the proposal with the lowest cost. |
|  | 6.2 | Format for Submitting Cost Proposals |
|  |  | Submit cost proposal on Attachment G. Include costing information on the bill of materials if possible. |
|  | 6.3 | Fixed Price Period |
|  |  | All prices, costs, and conditions outlined in the proposal shall remain fixed and valid for acceptance for 90 days starting on the due date for proposals. |

| 7.0 | SPECIAL CONTRACT TERMS AND CONDITIONS |
| --- | --- |
|  | 7.1 | Living Wage Requirement |
|  |  | All employees working on this project are covered by the Dane County Living Wage Ordinance Section 25.015 (d). See Section 28.0 Standard Terms and Conditions. The minimum living wage rate for 2015 is $11.47. The successful proposer will be required to sign a Living Wage Certification upon completion of the contract. Details are available on the Dane County Purchasing Division web site at www.co.dane.wi.us/purch/purch.htm |
|  | 7.2 | Domestic Partner Equal Benefits Requirement |
|  |  | The contractor [or grant beneficiary] agrees to provide the same economic benefits to all of its employees with domestic partners as it does to employees with spouses, or the cash equivalent if such a benefit cannot reasonably be provided. The contractor [or grant beneficiary] agrees to make available for County inspection the contractor's payroll records relating to employees providing services on or under this contract or subcontract [or grant]. If any payroll records of a contractor [or grant beneficiary] contain any false, misleading or fraudulent information, or if a contractor [or grant beneficiary] fails to comply with the provisions of s. 25.016, D. C. Ords., the contract compliance officer may withhold payments on the contract; terminate, cancel or suspend the contract in whole or in part; or, after a due process hearing, deny the contractor the right to participate in bidding on future County contracts for a period of one year after the first violation is found and for a period of three years after a second or subsequent violation is found |
|  | 7.3 | Local Purchasing Ordinance |
|  |  | Under County ordinances, a Local Vendor is defined as a supplier or provider of equipment, materials, supplies or services that has an established place of business within the County of Dane. An established place of business means a physical office, plant or other facility. A post office box address does not qualify a vendor as a Local Vendor. County ordinance provides that a local vendor automatically receive five points toward the evaluation score and vendors located within the counties adjacent to Dane County (Columbia, Dodge, Green, Iowa, Jefferson, Rock, Sauk) automatically receive two points toward the evaluation score. |

|  | 7.4 | Dane County Sustainability Principles |
| --- | --- | --- |
|  |  | On October 18, 2012, the Dane County Board of Supervisors adopted Resolution 103, 2012-2013 establishing the following sustainability principles for the county: Reduce and eventually eliminate Dane County government’s contribution to fossil fuel dependence and to wasteful use of scarce metals and minerals; Reduce and eventually eliminate Dane County government’s contribution to dependence upon persistent chemicals and wasteful use of synthetic substances; Reduce and eventually eliminate Dane County government’s contribution to encroachment upon nature and harm to life-sustaining ecosystems (e.g., land, water, wildlife, forest, soil, ecosystems); and Reduce and eventually eliminate Dane County government’s contribution to conditions that undermine people’s ability to meet their basic human needs. |
| 8.0 | REQUIRED FORMS |
|  | The following forms must be completed and submitted with the proposal in accordance with the instructions given in Section 2.0. Blank forms are attached. |
|  | Attachment A | Signature Affidavit |
|  | Attachment B | Vendor Registration Certification |
|  | Attachment C | Reference Data Sheet |
|  | Attachment D | Designation of Confidential and Proprietary Information |
|  | Attachment E | Fair Labor Practices Certification |
|  | Attachment F | Vendor Data Sheet |
|  | Attachment G | Cost Summary Page |

Attachment A

Submit With RFP

| RFP COVER PAGE SIGNATURE AFFIDAVIT |
| --- |
| NAME OF FIRM: |  |

In signing this proposal, we also certify that we have not, either directly or indirectly, entered into any agreement or participated in any collusion or otherwise taken any action in restraint of free competition; that no attempt has been made to induce any other person or firm to submit or not to submit a proposal; that this proposal has been independently arrived at without collusion with any other proposer, competitor or potential competitor; that this proposal has not been knowingly disclosed prior to the opening of proposals to any other proposer  or competitor; that the above statement is accurate under penalty of perjury.

The undersigned, submitting this proposal hereby agrees with all the terms, conditions, and specifications required by the County in this Request for Proposal, and declares that the attached proposal and pricing are in conformity therewith.

_____________________________________			_______________________

Signature 								Title

_____________________________________			_______________________

Name (type or print							Date

- Addendums -This firm herby acknowledges receipt / review of the following addendum(s)  (If any)

Addendum #_____ Addendum #_____Addendum #_____Addendum #_____

Attachment  B

Submit With RFP

VENDOR REGISTRATION CERTIFICATION

Per Dane County Ordinance, Section 62.15, “Any person desiring to bid on any county contract must register with the purchasing manager and pay an annual registration fee of $20.”

Your completed Vendor Registration Form and Registration Fee must be received for your bid to be considered for an award. Your bid/proposal may not be evaluated for failure to comply with this provision.

Complete a registration form online by visiting our web site at www.danepurchasing.com.. You will prompted to create a username and a password and you will receive a confirmation message, than log back in and complete the registration. Once your registration is complete you will receive a second confirmation. Retain your user name and password for ease of

re-registration in future years.

Payment may be made via credit card on-line or by check in the mail or in person at the Purchasing Division office. If paying by check make check payable to Dane County Treasurer and indicate your federal identification number (FIN) on the subject line.

### CERTIFICATION

The undersigned, for and on behalf of the PROPOSER, BIDDER OR APPLICANT named herein, certifies as follows:

- This firm is a paid, registered vendor with Dane County in accordance with the bid terms and conditions.

Vendor Number #_________			Paid until ________________________

Date Signed:                          	 	________________________________

Officer or Authorized Agent

_________________________________

Business Name

Attachment C

Submit With RFP

| REFERENCE DATA SHEET |
| --- |
| Provide company name, address, contact person, telephone number, and appropriate information on the product(s) and/or service(s) used for three (3) or more installations/services with requirements similar to those included in this solicitation document |
| NAME OF FIRM: |  |
| STREET ADDRESS: |  |
| CITY, STATE, ZIP |  |
| CONTACT PERSON: |  | EMAIL: |
| PHONE #: |  | FAX #: |
| Product(s) and/or Service(s) Used: |  |
| NAME OF FIRM: |  |
| STREET ADDRESS: |  |
| CITY, STATE, ZIP |  |
| CONTACT PERSON: |  | EMAIL: |
| PHONE #: |  | FAX #: |
| Product(s) and/or Service(s) Used: |  |
| NAME OF FIRM: |  |
| STREET ADDRESS: |  |
| CITY, STATE, ZIP |  |
| CONTACT PERSON: |  | EMAIL: |
| PHONE #: |  | FAX #: |
| Product(s) and/or Service(s) Used: |  |

Attachment D

Submit with RFP

| Designation of Confidential and Proprietary Information |
| --- |
| The attached material submitted in response to this Proposal includes proprietary and confidential information which qualifies as a trade secret, as provided in Sect 19.36(5), Wisconsin State Statutes, or is otherwise material that can be kept confidential under the Wisconsin Open Records law. As such, we ask that certain pages, as indicated below, of this proposal response be treated as confidential material and not be released without our written approval. Attach additional sheets if needed. |
| Section | Page Number | Topic |

Check mark :______This firm is not designating any information as proprietary and confidential  witch qualifies as trade secrete.

Prices always become public information when proposals are opened, and therefore cannot be designated as confidential.

Other information cannot be kept confidential unless it is a trade secret.  Trade secret is defined in Sect. 134(80)(1)(c) Wis. State Statutes, as follows: "Trade secret" means information, including a formula, pattern, compilation, program, device, method technique or process to which all of the following apply:

- The information derives independent economic value, actual or potential, from not being generally known to, and not being readily ascertainable by proper means by other persons who can obtain economic value from its disclosure or use.

- The information is the subject of efforts to maintain its secrecy that are reasonable under the circumstances.

In the event the Designation of Confidentiality of this information is challenged, the undersigned hereby agrees to provide legal counsel or other necessary assistance to defend the Designation of Confidentiality.

Failure to include this form in the proposal response may mean that all information provided as part of the proposal response will be open to examination or copying. The County considers other markings of confidential in the proposal document to be insufficient. The undersigned agree to hold the County harmless for any damages arising out of the release of any material unless they are specifically identified above.

_____________________________________			_______________________

Signature 								Title

_____________________________________			_______________________

Name (type or print							Date

Attachment E

Submit with RFP

FAIR LABOR PRACTICES CERTIFICATION Dane County Ordinance 25.11(28)

The undersigned, for and on behalf of the PROPOSER, BIDDER OR APPLICANT named herein, certifies as follows:

1.   That he or she is an officer or duly authorized agent of the above-referenced PROPOSER, BIDDER OR APPLLICANT, which has a submitted a proposal, bid or application for a contract with the county of Dane.

That PROPOSER, BIDDER OR APPLLICANT has:  (Check One)

________ not been found by the National Labor Relations Board (“NLRB”)  or the Wisconsin Employment Relations Commission (“WERC”) to have violated any statute or regulation regarding labor standards or relations in the seven years prior to the date this Certification is signed.

________ been found by the National Labor Relations Board (“NLRB”)  or the Wisconsin Employment Relations Commission (“WERC”) to have violated any statute or regulation regarding labor standards or relations in the seven years prior to the date this Certification is signed

Date Signed:                          	 		_________________________________

Officer or Authorized Agent

_________________________________

Business Name

NOTE:  You can find information regarding the violations described above at:  www.nlrb.gov  and http://werc.wi.gov.

For Reference Dane County Ord. 28.11 (28) is as follows:

(28) BIDDER RESPONSIBILITY. (a) Any bid, application or proposal for any contract with the county, including public works contracts regulated under chapter 40, shall include a certification indicating whether the bidder has been found by the National Labor Relations Board (NLRB) or the Wisconsin Employment Relations Committee (WERC) to have violated any statute or regulation regarding labor standards or relations within the last seven years. The purchasing manager shall investigate any such finding and make a recommendation to the committee, which shall determine whether the conduct resulting in the finding affects the bidder’s responsibility to perform the contract.

If you indicated that you have been found by the NLRB or WERC to have such a violation, you must include a copy of any relevant information regarding such violation with your proposal, bid or application.

Attachment F

Submit with RFP

VENDOR DATA SHEET / LOCAL PURCHASING PROVISIONS

| This address will be used to determine local purchasing preference and the mailing address where County purchase orders/contracts will be mailed: |
| --- |
| 1. | Company Name: |
| ADDRESS: |
| CITY: | COUNTY: |
| STATE: | ZIP+4: |
| TEL: | TOLL FREE TEL: | FAX: |
| 2. | Contact person in the event there are questions about your bid/proposal |
| NAME | TITLE: |
| TEL | TOLL FREE TEL |
| FAX | E-MAIL |
| 3. | Local Vendor: |
| Are you claiming a local purchasing preference under DCO 25.11(8) based on your response to section 1 of this form? ( No – continue on to the next page ( Yes – complete the remainder of this form |
| Indicate if your firm/company has an established place of business located in any of the following Wisconsin Counties. An established place of business means a physical office, plant or other facility. A post office box address does not qualify a vendor as a Local Vendor. DCO 25.04(7h) Select one: |
| We are claiming a 10% preference as a Dane County Business Dane County |
| We are claiming a 5% preference as a business located in a county adjacent to Dane County |
| ( Columbia County | ( Dodge County | ( Green County | ( Iowa County |
| ( Jefferson County | ( Rock County | ( Sauk County |  |

REVISED 9/12

Attachment G

Submit with RFP

| COST / FINANCIAL PROPOSAL |
| --- |
| NAME OF FIRM: |  |

Project Cost: 	$______________________

Alternate #1: Cost to remove and replace one existing faceplate and XLR connection in Main Exhibit Hall or Meeting Rooms with new XLR connection:

$______________________

Alternate #2: Cost to rotate existing AV racks #3 and #4 180 degrees in place:

$_______________

Service contract  to include pricing for five years following the initial one year warranty period. Please detail what is included with this service contract.

Year One – included, warranty period

Year Two 	$_____________________

Year Three 	$____________________

Year Four 	$_____________________

Year Five 	$_____________________

Maintenance to include hourly rates for ongoing maintenance and repairs, outside of the service contract, including a markup for parts. Pricing for five years is requested.

Parts discount from list   __________%

| Year | Hourly Rate | Overtime Rate |
| --- | --- | --- |
| One | $ | $ |
| Two | $ | $ |
| Three | $ | $ |
| Four | $ | $ |
| Five | $ | $ |

STANDARD TERMS AND CONDITIONS (Request For Bids/Proposals/Contracts) Dane County Purchasing Division Rev. 11/13

1.0	APPLICABILITY:  The terms and conditions set forth in this document apply to Requests for Proposals (RFP), Bids and all other transactions whereby the County of Dane acquires goods or services, or both.

1.1	ENTIRE AGREEMENT:  These Standard Terms and Conditions shall apply to any contract, including any purchase order, awarded as a result of this request.  Special requirements of a resulting contract may also apply.  Said written contract with referenced parts and attachments shall constitute the entire agreement, and no other terms and conditions in any document, acceptance, or acknowledgment shall be effective or binding unless expressly agreed to in writing by the County.  Unless otherwise stated in the agreement, these standard terms conditions supersede any other terms and/or conditions applicable to this agreement.

1.2	DEFINITIONS:  As used herein, “vendor” includes a provider of goods or services, or both, who is responding to an RFP or a bid, and “bid” includes a response to either an RFP or a bid.

2.0	SPECIFICATIONS:  The specifications herein are the minimum acceptable.  When specific manufacturer and model numbers are used, they are to establish a design, type of construction, quality, functional capability or performance level, or any combination thereof, desired.  When alternates are proposed, they must be identified by manufacturer, stock number, and such other information necessary to establish equivalency.  Dane County shall be the sole judge of equivalency.  Vendors are cautioned to avoid proposing alternates to the specifications that may result in rejection of their bid.

3.0	DEVIATIONS AND EXCEPTIONS:  Deviations and exceptions from terms, conditions, or specifications shall be described fully on the vendor’s letterhead, signed, and attached to the bid.  In the absence of such statement, the bid shall be accepted as in strict compliance with all terms, conditions, and specifications and vendor shall be held liable for injury resulting from any deviation.

4.0	QUALITY:  Unless otherwise indicated in the request, all material shall be first quality.  No pre-owned, obsolete, discontinued or defective materials may be used.

5.0	QUANTITIES:  The quantities shown herein are based on estimated needs.  The County reserves the right to increase or decrease quantities to meet actual needs.

6.0	DELIVERY:  Deliveries shall be FOB destination freight prepaid and included unless otherwise specified.  County will reject shipments sent C.O.D. or freight collect.

7.0	PRICING:  Unit prices shown on the bid shall be the price per unit of sale as stated on the request or contract.  For any given item, the quantity multiplied by the unit price shall establish the extended price, the unit price shall govern in the bid evaluation and contract administration.

7.1	Prices established in continuing agreements and term contracts may be lowered due to market conditions, but prices shall not be subject to increase for the term specified in the award.  Vendor shall submit proposed increases to the contracting department thirty (30) calendar days before the proposed effective date of the price increase.  Proposed increases shall be limited to fully documented cost increases to the vendor that are demonstrated to be industry wide.  Price increases may not be granted unless they are expressed in bid documents and contracts or agreements.

7.2	Submission of a bid constitutes bidder’s certification that no financial or personal relationship exists between the bidder and any county official or employee except as specially set forth in writing attached to and made a part of the bid.  The successful bidder shall disclose any such relationship which develops during the term of the contract.

8.0	ACCEPTANCE-REJECTION:  Dane County reserves the right to accept or reject any or all bids, to waive any technicality in any bid submitted and to accept any part of a bid as deemed to be in the best interests of the County.  Submission of a proposal or a bid constitutes the making of an offer to contract and gives the County an option valid for 60 days after the date of submission to the County.

8.1	Bids MUST be dated and time stamped by the Dane County Purchasing Division Office on or before the date and time that the bid is due.  Bids deposited or time stamped in another office will be rejected.  Actual receipt in the office of the purchasing division is necessary; timely deposit in the mail system is not sufficient.  THERE WILL BE NO EXCEPTIONS TO THIS POLICY.

9.0	METHOD OF AWARD:  Award shall be made to the lowest responsible responsive vendor conforming to specifications, terms, and conditions, or to the most advantageous bid submitted to the County on a quality versus price basis.

10.0	ORDERING/ACCEPTANCE:  Written notice of award to a vendor in the form of a purchase order or other document, mailed or delivered to the address shown on the bid will be considered sufficient notice of acceptance of bid.  A formal contract containing all provisions of the contract signed by both parties shall be used when required by the Dane County Purchasing Division.

11.0	PAYMENT TERMS AND INVOICING:  Unless otherwise agreed, Dane County will pay properly submitted vendor invoices within thirty (30) days of receipt of goods and services.  Payment will not be made until goods or services are delivered, installed (if required), and accepted as specified.  Invoices presented for payment must be submitted in accordance with instructions contained on the purchase order.

11.1	NO WAIVER OF DEFAULT:  In no event shall the making of any payment or acceptance of any service or product required by this Agreement constitute or be construed as a waiver by County of any breach of the covenants of the Agreement or a waiver of any default of the successful vendor, and the making of any such payment or acceptance of any such service or product by County while any such default or breach shall exist shall in no way impair or prejudice the right of County with respect to recovery of damages or other remedy as a result of such breach or default.

12.0	TAXES:  The County and its departments are exempt from payment of all federal tax and Wisconsin state and local taxes on its purchases except Wisconsin excise taxes as described below.  The State of Wisconsin Department of Revenue has issued tax exempt number ES41279 to Dane County.

12.1	The County is required to pay the Wisconsin excise or occupation tax on its purchase of beer, liquor, wine, cigarettes, tobacco products, motor vehicle fuel and general aviation fuel.  The County is exempt from Wisconsin sales or use tax on these purchases.  The County may be subject to other states’ taxes on its purchases in that state depending on the laws of that state.  Vendors performing construction activities are required to pay state use tax on the cost of materials.

13.0	GUARANTEED DELIVERY:  Failure of the vendor to adhere to delivery schedules as specified or to promptly replace rejected materials shall render the vendor liable for all costs in excess of the contract price when alternate procurement is necessary.  Excess costs shall include administrative costs.

14.0	APPLICABLE LAW AND VENUE:  This contract shall be governed under the laws of the State of Wisconsin, and venue for any legal action between the parties shall be in Dane County Circuit Court.  The vendor shall at all times comply with and observe all federal  and state laws, local laws, ordinances, and regulations which are in effect during the period of this contract and which in any manner affect the work or its conduct.

15.0	ASSIGNMENT:  No right or duty in whole or in part of the vendor under this contract may be assigned or delegated without the prior written consent of Dane County.

16.0	NONDISCRIMINATION/AFFIRMATIVE ACTION:  During the term of this Agreement the vendor agrees, in accordance with sec. 111.321, Wis. Stats., and Chapter 19 of the Dane County Code of Ordinances, not to discriminate against any person, whether an applicant or recipient of services, an employee or applicant for employment, on the basis of age, race, ethnicity, religion, color, gender, disability, marital status, sexual orientation, national origin, cultural differences, ancestry, physical appearance, arrest record or conviction record, military participation or membership in the national guard, state defense force or any other reserve component of the military forces of the United States, or political beliefs.  The vendor shall provide a harassment-free work environment.  These provisions shall include, but not be limited to, the following:  employment, upgrading, demotion, transfer, recruitment, advertising, layoff, termination, training, including apprenticeships, rates of pay or other forms of compensation.

16.1	Vendors who have twenty (20) or more employees and a contract of twenty thousand dollars ($20,000) or more must submit a written affirmative action plan to the County’s Contract Compliance Officer within fifteen (15) working days of the effective date of the contract.  The County may elect to accept a copy of the current affirmative action plan filed with and approved by a federal, state or local government unit.

16.2	The vendor agrees to post in conspicuous places, available for employees and applicants for employment, notices setting forth the provisions of this Agreement as they relate to affirmative action and nondiscrimination.

16.3	Failure to comply with these Terms and Conditions may result in the vendor being debarred, termination of the contract and/or withholding of payment.

16.4	The vendor agrees to furnish all information and reports required by Dane County’s Contract Compliance Officer as the same relate to affirmative action and nondiscrimination, which may include any books, records, or accounts deemed appropriate to determine compliance with Chapter 19, D.C. Ords. and the provisions of this Agreement.

16.5	Americans with Disabilities Act:  The vendor agrees to the requirements of the ADA, providing for physical and programmatic access to service delivery and treatment in all programs and activities.

17.0	PATENT, COPYRIGHT AND TRADEMARK INFRINGEMENT:  The vendor guarantees goods sold to the County were manufactured or produced in accordance with applicable federal labor laws, and that the sale or use of the articles described herein do not infringe any patent, copyright or trademark.  The vendor covenants that it will, at its own expense, defend every suit which shall be brought against the County (provided that such vendor is promptly notified of such suit, and all papers therein are delivered to it) for any alleged infringement of any patent, copyright or trademark by reason of the sale or use of such articles, and agrees that it will pay all costs, damages, and profits recoverable in any such suit.

18.0	SAFETY REQUIREMENTS:  All materials, equipment, and supplies provided to the County must fully comply with all safety requirements as set forth by the Wisconsin Department of Commerce and all applicable OSHA Standards.

18.1	MATERIAL SAFETY DATA SHEET:  If any item(s) on an order(s) resulting from this award(s) is a hazardous chemical, as defined under 29 CFR 1910.1200, provide one (1) copy of the Material Safety Data Sheet for each item with the shipped container(s) and one (1) copy with the invoice(s).

19.0	WARRANTY: Unless specifically expressed otherwise in writing, goods and equipment purchased as a result of this request shall be warranted against defects by the vendor for one (1) year from date of receipt.  An equipment manufacturer’s standard warranty shall apply as a minimum and must be honored by the vendor.  The time limitation in this paragraph does not apply to the warranty provided in paragraph 27.0.

20.0 INDEMNIFICATION & INSURANCE.

20.1.	PROVIDER shall indemnify, hold harmless and defend COUNTY, its boards, commissions, agencies, officers, employees and representatives against any and all liability, loss (including, but not limited to, property damage, bodily injury and loss of life), damages, costs or expenses which COUNTY, its officers, employees, agencies, boards, commissions and representatives may sustain, incur or be required to pay by reason of PROVIDER furnishing the services or goods required to be provided under this Agreement, provided, however, that the provisions of this paragraph shall not apply to liabilities, losses, charges, costs, or expenses caused by or resulting from the acts or omissions of COUNTY, its agencies, boards, commissions, officers, employees or representatives.  The obligations of PROVIDER under this paragraph shall survive the expiration or termination of this Agreement.

20.2.	In order to protect itself and COUNTY, its officers, boards, commissions, agencies, agents, volunteers, employees and representatives under the indemnity provisions of the subparagraph above, PROVIDER shall, at PROVIDER’s own expense, obtain and at all times during the term of this Agreement keep in full force and effect the insurance coverages, limits, and endorsements listed below.  When obtaining required insurance under this Agreement and otherwise, PROVIDER agrees to preserve COUNTY’s subrogation rights in all such matters that may arise that are covered by PROVIDER’s insurance.  Neither these requirements nor the COUNTY’s review or acceptance of PROVIDER’s certificates of insurance is intended to limit or qualify the liabilities or obligations assumed by the PROVIDER under this Agreement. The County expressly reserves the right to require higher or lower insurance limits where County deems necessary.

20.2.1.	Commercial General Liability.

PROVIDER agrees to maintain Commercial General Liability insurance at a limit of not less than $1,000,000 per occurrence.  Coverage shall include, but not be limited to, Bodily Injury and Property Damage to Third Parties, Contractual Liability, Personal Injury and Advertising Injury Liability, Premises-Operations, Independent PROVIDERs and Subcontractors, and Fire Legal Liability.  The policy shall not exclude Explosion, Collapse, and Underground Property Damage Liability Coverage.  The policy shall list DANE COUNTY as an Additional Insured.

20.2.2.	Commercial/Business Automobile Liability.

PROVIDER agrees to maintain Commercial/Business Automobile Liability insurance at a limit of not less than $1,000,000 Each Occurrence. PROVIDER further agrees coverage shall include liability for Owned, Non-Owned & Hired automobiles. In the event PROVIDER does not own automobiles, PROVIDER agrees to maintain coverage for Hired & Non-Owned Auto Liability, which may be satisfied by way of endorsement to the Commercial General Liability policy or separate Business Auto Liability policy.

20.2.3.	Environmental Impairment (Pollution) Liability

PROVIDER agrees to maintain Environmental Impairment (Pollution) Liability insurance at a limit of not less than $1,000,000 per occurrence for bodily injury, property damage, and environmental cleanup costs caused by pollution conditions, both sudden and non-sudden.  This requirement can be satisfied by either a separate environmental liability policy or through a modification to the Commercial General Liability policy.  Evidence of either must be provided.

20.2.4.	Workers’ Compensation.

PROVIDER agrees to maintain Workers Compensation insurance at Wisconsin statutory limits.

20.2.5.	Umbrella or Excess Liability.

PROVIDER may satisfy the minimum liability limits required above for Commercial General Liability and Business Auto Liability under an Umbrella or Excess Liability policy.  There is no minimum Per Occurrence limit of liability under the Umbrella or Excess Liability; however, the Annual Aggregate limit shall not be less than the highest “Each Occurrence” limit for the Commercial General Liability and Business Auto Liability.  PROVIDER agrees to list DANE COUNTY as an “Additional Insured” on its Umbrella or Excess Liability policy.

20.3.	Upon execution of this Agreement, PROVIDER shall furnish COUNTY with a Certificate of Insurance listing COUNTY as an additional insured and, upon request, certified copies of the required insurance policies.  If PROVIDER's insurance is underwritten on a Claims-Made basis, the Retroactive Date shall be prior to or coincide with the date of this Agreement, the Certificate of Insurance shall state that professional malpractice or errors and omissions coverage, if the services being provided are professional services coverage is Claims-Made and indicate the Retroactive Date, PROVIDER shall maintain coverage for the duration of this Agreement and for six (6) years following the completion of this Agreement.  PROVIDER shall furnish COUNTY, annually on the policy renewal date, a Certificate of Insurance as evidence of coverage.  It is further agreed that PROVIDER shall furnish the COUNTY with a 30-day notice of aggregate erosion, in advance of the Retroactive Date, cancellation, or renewal.  It is also agreed that on Claims-Made policies, either PROVIDER or COUNTY may invoke the tail option on behalf of the other party and that the Extended Reporting Period premium shall be paid by PROVIDER.  In the event any action, suit or other proceeding is brought against COUNTY upon any matter herein indemnified against, COUNTY shall give reasonable notice thereof to PROVIDER and shall cooperate with PROVIDER's attorneys in the defense of the action, suit or other proceeding.  PROVIDER shall furnish evidence of adequate Worker's Compensation Insurance. In case of any sublet of work under this Agreement, PROVIDER shall furnish evidence that each and every subcontractor has in force and effect insurance policies providing coverage identical to that required of PROVIDER.  In case of any sublet of work under this Agreement, PROVIDER shall furnish evidence that each and every subcontractor has in force and effect insurance policies providing coverage identical to that required of PROVIDER.

20.4.	The parties do hereby expressly agree that COUNTY, acting at its sole option and through its Risk Manager, may waive any and all requirements contained in this Agreement, such waiver to be in writing only.  Such waiver may include or be limited to a reduction in the amount of coverage required above.  The extent of waiver shall be determined solely by COUNTY's Risk Manager taking into account the nature of the work and other factors relevant to COUNTY's exposure, if any, under this Agreement.

21.0	CANCELLATION:  County reserves the right to terminate any Agreement due to non-appropriation of funds or failure of performance by the vendor.  This paragraph shall not relieve County of its responsibility to pay for services or goods provided or furnished to County prior to the effective date of termination.

22.0	PUBLIC RECORDS ACCESS:  It is the intention of the County to maintain an open and public process in the solicitation, submission, review, and approval of procurement activities.  Bid openings are public unless otherwise specified.  Records are not available for public inspection prior to issuance of the notice of intent to award or the award of the contract.  Bid results may be obtained by visiting the Dane County Purchasing Office Monday – Friday, between 8:00 a.m. and 4:00 p.m.  Prior appointment is advisable.

22.1	PROPRIETARY INFORMATION:  If the vendor asserts any of its books and records of its business practices and other matters collectively constitute a trade secret as that term is defined in s. 134.90(1)(c), Wis. Stats., County will not release such records to the public without first notifying the vendor of the request for the records and affording the vendor an opportunity to challenge in a court of competent jurisdiction the requester’s right to access such records.  The entire burden of maintaining and defending the trade secret designation shall be upon the vendor.  The vendor acknowledges and agrees that if the vendor shall fail, in a timely manner, to initiate legal action to defend the trade secret designation or be unsuccessful in its defense of that designation, County shall be obligated to and will release the records.

22.2	Any material submitted by the vendor in response to this request that the vendor considers confidential and proprietary information and which vendor believes qualifies as a trade secret, as provided in section 19.36(5), Wis. Stats., must be identified on a designation of Confidential and Proprietary Information form.  Pricing will not be held confidential after award of contract.

22.3	Data contained in a bid, all documentation provided therein, and innovations developed as a result of the contracted commodities or services cannot be copyrighted or patented.  All data, documentation, and innovations shall be the property of the County.

23.0	RECYCLED MATERIALS:  Dane County is required to purchase products incorporating recycled materials whenever technically and economically feasible.  Vendors are encouraged to bid products with recycled content which meet specifications.

24.0	PROMOTIONAL ADVERTISING:  Reference to or use of Dane County, any of its departments or sub-units, or any county official or employee for commercial promotion is prohibited.

25.0	ANTITRUST ASSIGNMENT:  The vendor and the County of Dane recognize that in actual economic practice, overcharges resulting from antitrust violation are in fact usually borne by the Purchaser.  Therefore, the successful vendor hereby assigns to the County of Dane any and all claims for such overcharges as to goods, materials or services purchased in connection with this contract.

26.0	RECORDKEEPING AND RECORD RETENTION-PUBLIC WORKS CONTRACTS:  The successful bidder on a public works contract shall comply with the State of Wisconsin prevailing wage scale and shall establish and maintain adequate payroll records for all labor utilized as well as records for expenditures relating to all subcontracts, materialmen and suppliers.  All records must be kept in accordance with generally accepted accounting procedures.  The County shall have the right to audit, review, examine, copy, and transcribe any such records or documents.  The vendor will retain all documents applicable to the contract for a period of not less than three (3) years after final payment is made.

26.1	RECORDKEEPING AND RECORD RETENTION-COST REIMBURSEMENT CONTRACTS:  Where payment to the vendor is based on the vendor’s costs, vendor shall establish and maintain adequate records of all expenditures incurred under the contract.  All records must be kept in accordance with generally accepted accounting procedures.  The County contracting agency shall have the right to audit, review, examine, copy, and transcribe any pertinent records or documents relating to any contract resulting from this bid/proposal held by the vendor.  The vendor will retain all documents applicable to the contract for a period of not less than three (3) years after final payment is made.

27.0	LIVING WAGE REQUIREMENT:  The vendor shall, where appropriate, comply with the County’s Living Wage requirements as set forth in section 25.015, Dane County Ordinances.

27.01	In the event its payroll records contain any false, misleading or fraudulent information, or if the vendor fails to comply with the provisions of s. 25.015, D.C. Ords., the County may withhold payments on the contract, terminate, cancel or suspend the contract in whole or in part, or, after a due process hearing, deny the vendor the right to participate in bidding on future County contracts for a period of one (1) year after the first violation is found and for a period of three (3) years after a second violation is found.

27.02	Bidders are exempt from the requirement of this section if:

- The maximum value of services to be provided is less than $5,000;

- The bid involves only the sale of goods to the County;

- The bid is for professional services;

- The bid is for a public works contract where wages are regulated under s. 62.293, Wis. Stats.;

- The bidder is a school district, a municipality, or other unit of government;

- The service to be provided is residential services at an established per bed rate;

- The bidder’s employees are persons with disabilities working in employment programs and the successful bidder holds a current sub-minimum wage certificate issued by the U.S. Department of Labor or where such a certificate could be issued but for the fact that the employer is paying a wage higher than the minimum wage;

- The bidder is an individual providing services to a family member; or

- The bidder’s employees are student interns.

27.03 COMPLIANCE WITH FAIR LABOR STANDARDS. During the term of this Agreement, PROVIDER shall report  to the County Contract Compliance Officer, within ten (10) days, any allegations to, or findings by the National Labor Relations Board (NLRB) or Wisconsin Employment Relations commission (WERC) that PROVIDER has violated a statute or regulation regarding labor standards or relations within the seven years prior to entering this Agreement.   If an investigation by the Contract Compliance Officer results in a final  determination that the matter adversely affects PROVIDER’S responsibilities under this Agreement, and which recommends termination, suspension or cancellation of this agreement, the County may take such action.

27.04  PROVIDER may appeal any adverse finding by the Contract Compliance Officer as set forth in sec. 25.015(11)(c) through (e).

27.05  PROVIDER shall post the following statement in a prominent place visible to employees:  “As a condition of receiving and maintaining a contract with Dane County, this employer shall comply with federal, state and all other applicable laws prohibiting retaliation for union organizing.”

APPENDIX 1

SECTION 27 40 00

AUDIO-VISUAL SYSTEMS

- – GENERAL

SECTION INCLUDES

Contractor qualifications

Equipment standards

Systems descriptions

Training, documentation

RELATED WORK

Drawings and general provisions of the Contract, including General Conditions and other requirements of the RFP apply to the work of this section.

Section 27 05 00 - Common Work Results for Communications Systems

SUBMITTALS

Three (3) printed sets of completed shop drawings shall be provided for consultant's approval. In addition, drawings may be provided in electronic form (.DWG format) on CD. CONTRACTOR SHALL NOT PROCURE EQUIPMENT OR BEGIN WORK ON THIS PROJECT UNTIL SHOP DRAWINGS HAVE BEEN SUBMITTED AND APPROVED.

Submittal documents must be provided within 30 days of award of contract, or sooner if necessary to comply with construction schedule. Contractor is solely responsible for all costs resulting from delay in providing shop drawings in a timely manner.

These submittals or shop drawings shall include:

A complete equipment list of all components including quantities.

Manufacturer's catalog specification cuts and printed descriptive literature on all components being provided.

A complete list of all cable runs including termination locations and numbers/identification schedule.

Schematic drawings of all system wiring. The diagrams shall show schematic wiring of the equipment and all connections to be made to devices. Terminal connections in the equipment shall be numbered to correspond to the diagrams for use in making connections. Wiring diagrams shall be coordinated so that terminal numbering, circuit designation and equipment or device designations are the same on all drawings. All drawings must be submitted and approved by the Consultant before fabrication starts, but such approval will not waive any specification requirements unless so specifically stated. Final approval will be made after checking the equipment when operated in the field. For submittals, all of the above drawings shall be made on 24" x 36" reproducible media.

Manufacturer cut sheets are acceptable.

PERFORMANCE TESTING

Testing of all installed cable and equipment shall be performed by the contractor as soon as practical after equipment is installed.

All cable and equipment shall be tested with state-of-the-art, industry standard test equipment by personnel properly trained to operate equipment.

Testing shall be accomplished before notifying Engineer of substantial completion and before punch list is performed.

A performance checklist shall be created by contractor to document operation and testing of all equipment.  Checklist shall be delivered to Engineer prior to punch list and project acceptance.

WORK INCLUDES

All labor, materials, equipment, tools and services required to perform all work and services for execution, installation and completion of all Audio-Visual work including all parts lists, operating instructions, and wiring diagrams shown on the drawings and as specified and completely coordinated with all other trades.

All supplementary or miscellaneous items, appurtenances and devices incidental to or necessary for a sound, secure and complete communications installation.

Complete and in operative condition and to approval of Architect/Engineer, materials described herein and shown on drawings.

Coordination with other trades as required.

Complete adherence to equipment manufacturer’s recommendations to assure complete, optimal operation.  Contractor shall notify Engineer where such recommendations appear to contradict project documents.

Equipment, materials and accessories for communications systems as shown and noted on the drawings including but not limited to the following in each of four (4) existing AV rooms:

      - Remove existing audio mixer(s)

      - Provide new audio DSP with input/output cards

      - Provide new control system

      - Provide PoE injectors as required and coordinate with owner to utilize existing Ethernet infrastructure for audio transport between AV rooms and other site buildings

      - Provide new 10” touch screen user interface

      - Provide custom rack panel with cutout for touch screen

      - Patch cables, connectors, hardware, programming and installation

      - Testing, balancing and tuning of speakers in Exhibit Hall A, B, C, D and Lobby, all meeting rooms on upper level and all lower level meeting rooms M1-M8 with atrium.

WORK BY OWNER

Owner may provide certain electronic equipment not indicated on project documents.

Owner means authorized representatives of Dane County Alliant Energy Center.

Owner will provide any required data cable (copper or fiber) that is required to connect any two different AV rooms or on-site buildings that is over 50 feet in length.

DESCRIPTION

This section covers general requirements associated with the installation of audiovisual systems within the project. Refer to sections listed below for more specific system requirements. Multiple spaces (rooms) with multiple systems may be covered under this section.

Furnish all materials and labor to provide complete and professionally installed systems in working order.  Programming and functionality of the AV systems will be the responsibility of the AV Contractor(s).  The AV Contractor(s) is expected to work in conjunction with the Owner's Staff to complete the system installation to owner's satisfaction.

Systems are noted on project documents (drawings).  Dark line weights indicate all equipment to be provided by contractor.  Light line weights or notes indicating “existing” may be assumed to be existing and not provided by contractor.  Contractor to reuse or tie into existing systems.

Discrepancies between specifications, drawings or RFP language are to be immediately brought to the attention of the Engineer in the form of an RFI (Request for Information).  For bidding purposes assume the greater quantity or higher quality in case of a discrepancy.

AV Contractor(s) shall provide any and all connectors, cable, hardware, transformers, power supplies, rack panels, interfaces, fasteners, wire harnessing materials, bushings and any other incidentals required for complete and proper functioning of this system whether or not they are specifically listed, shown or described.

Owner's Staff may review and field verify exact locations of equipment placement with the AV contractor  prior to installation. This does not relieve the contractor from performing his due diligence in installing equipment per manufacturer's recommendations and delivering a completely functioning system.

Additional information concerning the design intent is contained both within this document and on AV system drawings.

Where conflicts exist between drawings and specifications, the contractor must bring the discrepancies to the project AE's attention no later than ten (10) days before the bid due date, or, if noticed after the bid award, prior to installation of equipment.  Contractor shall deliver a completely functioning system regardless of discrepancies in the documents.

As part of the contract for this work, the AV Contractor(s) shall be required to submit to the Owner a listing of the date or dates that it intends to purchase the audiovisual equipment specified in this section.

Date(s) submitted shall be coordinated with the project schedule presented by the general contractor (or Owner/Engineer). Purchase date(s) shall be within 6 months of the time the equipment is intended to be installed in the building.

The Owner reserves the right to negotiate these dates with the AV contractor. After these dates are agreed upon, the, AV contractor shall not purchase any equipment prior to these dates without written permission from the Owner.

The Owner recognizes the AV equipment specified is rapidly changing. The intent of this requirement is to allow the Owner the option of upgrading the equipment to models that are more current to the time of installation.

In the case of a manufacturer discontinuing the manufacture of a certain piece of equipment required by this project, the contractor shall provide a new submittal for a new product that is the newer version of the discontinued product from the same manufacturer.

Any changes made to the equipment specifications after bidding that result in increased cost will be considered changes to the contract and will be processed accordingly.  The change in cost resulting from owner selecting a more current projector model shall be handled as follows:

The manufacturer's suggested retail price (MSRP) of the bid product shall be obtained.

The MSRP of the new model selected by owner shall be obtained.

The difference between the MSRP of the two models shall be calculated.

If the change in MSRP between bid model and new model is positive, that shall be the amount of the change order due to the contractor.

If the change in MSRP is negative, that shall be the amount due as a credit to the owner.

Manufacturer's warranties to be in full effect for a minimum of one (1) year from substantial completion.

The work that is to be performed by the AV Contractor(s) under this specification shall include the provision of equipment noted in above paragraphs and below in section 2 – Products to permit the routing of audio signals from a source in and AV to any other AV room and its associated venues.  This includes routing to other buildings on the site that have network connections.

Contractor is to coordinate with owner and utilize their existing Ethernet network to connect the AV rooms and other buildings.

The system shall use CobraNet protocol in conjunction with the owner’s network.

Each venue shall be tested, balanced and tuned for proper sound pressure level and coverage.

Pricing / Alternates

The project has only one phase and it will be completed as soon as possible without delay.  It is noted as the Main Project

The project has one add-alternate to provide a price to remove existing XLR jacks and replace them with new.

Maintenance Contract

Bidder shall identify as a separate price the cost of a 4-year maintenance contract.  Bidder shall identify the services proposed to be covered in the contract.

The contract shall include only hours related to servicing AV equipment, set up, programming, installation of new equipment and other related tasks.

The Owner may take responsibility for replacing failed equipment with new.  The contract should anticipate time required to replace or service equipment, but not to purchase new or replacement equipment. Additionally, the contract should contain a percentage discount from list pricing for equipment, should the County choose to purchase equipment through the contract during the four year term.

The bidder may consider pricing in small blocks of time (less than 4 years, but applicable to the 4-year period as an unchanging price) as in a unit bid.  In this way the Owner may select a certain number of time blocks according to their own risk assessment and budget availability. When a certain time block is used up the Owner may elect to purchase additional time blocks at the same rate until the 4-year period expires.

This 4-year period shall begin one year after substantial completion of the Main Project. The first year of failed equipment replacement should be covered by each manufacturer and the first year of vendor labor and maintenance should be covered in the base bid price, incurring no expense to the owner for the first year.

BIDDER QUALIFICATIONS

AV contractor(s) shall perform the entire work of this section. These contractors shall be regularly engaged in the installation and service of audiovisual systems including but not limited to those systems listed.

AV Contractors must meet the following qualifications.

Provide a written narrative describing how each of the following qualifications will be met:

Capability to provide all systems within full and strict compliance with all provisions of this specification.

Has been actively engaged in the installation of AV systems included under this section for a minimum of five years.

Be a certified a dealer of the products which they are installing.  Provide certification documentation.

AV contractor shall furnish as part of the proposal response, a list of five projects whose size, value, scope and complexity is similar to that being bid.  The minimum period of operation for each shall be 12 months. For each facility listed provide:

Name and location of installation.

Date of occupancy by Owner.

Owner's representative to contact and their telephone number.

Construction Manager or General Contractor and Architect's project manager and their telephone numbers.

AV contractor shall have access to all necessary equipment and has organizational capacity and technical competence necessary to enable performance of this work properly and expeditiously.

Contractor shall employ adequate number of skilled workers who are thoroughly trained and experienced in the necessary crafts and who are completely familiar with the specified requirements and the methods needed for proper performance of the work of this section.

Contractor shall provide a designated supervisor present and in charge on the project site during all phases of installation and testing of the system.

Contractor shall be prepared to furnish copies of the installation documents from a previous similar installation.

Contractor shall be prepared to furnish a list of test and calibration equipment for the servicing and alignment of AV systems.

Contractor shall have AutoCAD ability to create one-line shop drawings and accurate as-built record documents.

Contractor's compliment of equipment shall include, but is not limited to:

      - Equipment appropriate for testing and analyzing audio signals

      - Calibrated sound pressure level meter measuring in dB SPL

Has a record of satisfactorily completing past projects. Criteria that will be considered in determining satisfactory completion of project by Contractor will include:

      - Completed contracts in accordance with drawings and specifications.

      - Diligently pursued execution of the work and completed contracts according to the established time schedule unless the Owner grants extensions.

      - Fulfilled guarantee requirements of the Contract Documents.

The AV contractor supplying the equipment shall show satisfactory evidence that it maintains a fully equipped local service organization capable of furnishing adequate inspection and service to the systems, including replacement parts. The service organization shall be capable of a minimum 4 hour on site response time. The contractor shall produce evidence that it has had a fully experienced and established service organization for at least five (5) years and proven satisfactory installations during that time.

SERVICE

On-the-premises service, parts and labor is to be provided by AV contractor during normal working hours at no cost to the Owner, for a period of 12 months from the date of final acceptance. AV contractor must respond within 24 hours or the next business day to requests for service. AV contractor must also provide technical support via telephone at no charge during the warranty period.

On-the-premises service must also be made available at other than normal working hours, and shall be charged by the AV contractor's service representative at current labor rates minus normal hour rate.

The AV contractor shall maintain engineering and service departments capable of rendering advice regarding installation and final adjustment of the systems.

Provide a separate (alternate) price for a 4-year maintenance contract beyond the initial one year initial warranty.

MAINTENANCE AND OPERATING MANUALS

Upon project completion the Contractor shall provide four complete sets, in hard cover binders, of maintenance and operating instructions for this system and any software, CD-ROMs, DVDs or other materials provided by the manufacturer.  These manuals shall include the following:

A table of contents.

Simplified operational procedures with diagrams depicting the actual equipment front panels showing the nominal level settings for the controls.

Question and answer type trouble-shooting guides.

One copy of approved system As Built drawings.

The AV contractor shall maintain in their office a record of all original manual information to be able to issue as a replacement copy, at the Owner's expense, during the time the equipment is in actual service.

See General Requirements Division 01.

AS-BUILT CONSTRUCTION DRAWINGS

Existing as-builts of the facility are provided for reference.

New one-line drawings included with the specifications set shall be modified by the AV contractor to denote as-built information, and shall be included as part of the as-built documentation. As built documentation shall include a complete list of all cable runs including termination locations, numbers/identification, and test data as required under the section on commissioning.

The contractor shall produce new as-built drawings as required for equipment that currently has no drawings, such as rack elevations once project is complete. Rack elevations shall show (to scale) positions of all major equipment when facing the rack from the front.

The owner, through the Consultant, will provide a one-line in paper and electronic (".dwg", AutoCAD rel. 14) formats on which as-built construction information can be added. These documents will be modified accordingly by the contractor to denote as-built information as defined above and returned to the Consultant for acceptance. This information shall be supplied to the Consultant/Engineer no later than two (2) weeks after the completion of the project.

Also provided will be PDF versions of existing as-built drawings.  The contractor shall use these for planning purposes and to note which equipment has been removed or modified.

The Contractor shall annotate the base drawings and return to the Engineer in hard copy (same plot size as originals).  Hard copies AND electronic copies are REQUIRED.

Each drawing submitted by the Contractor as part of the Project Documentation shall be identified as an "As-built" drawing and include the following:

The Contractor name and/or logo

The date of the drawing

If electronic files are utilized, all fonts, color, layer, Model Space/Paper Space conventions established in the base drawings shall be retained by the Contractor in preparation of the As-built drawings.

If electronic files are utilized, prior to generation of the drawings, the Contractor shall provide a sample file and test plot to the Engineer for review and approval.

All documentation, including hard copy and electronic forms shall become the property of the Owner.

If drawings are submitted by AV contractor in electronic form as "As-builts" or "Record Drawings", they shall adhere to all CAD standards as outlined in the most recent edition of Engineer’s CAD standards manual which will be provided upon request.

– PRODUCTS

EQUIPMENT STANDARDS

Complete AV systems consisting of all the individual systems as shown and specified are required. Equivalent manufacturers and products shall be in strict accordance with this specification. Substitutions during the construction phase may be permitted only with prior approval from the Owner's Staff and in writing from the AV consultant.  For bidding purposes, no substitutions will be accepted or considered.  Bidders are to adhere strictly to the project documents.

It is the responsibility of the AV contractor to verify the completeness of the drawings, specifications and schedules and the suitability of devices to meet the intent of the specifications. Any additional equipment, accessories or incidentals required, whether or not specifically mentioned herein, shall be provided by the contractor without claim for additional payment, it being understood that a complete operational system is required.

All materials and equipment shall be new and unused.  Unless specifically approved by the Consultant, all materials and equipment in the system shall be the standard design or model ordinarily supplied as a product item by manufacturers regularly engaged in the production of such equipment.  They shall be the manufacturer's latest standard designs current at the time of delivery, modified only to the extent necessary to comply with the requirements of these specifications. Where two or more units of the same class of equipment are required, such units shall be the standard product of a single manufacturer, but individual classes of compatible equipment may be the products of different manufacturers. Manufacturers shall be established in the industry so that prompt and continued service and delivery of spare parts may be assured.

All equipment quantities listed in audiovisual specification sections are for reference only and could vary depending on the type of manufacturer equipment provided. Refer to schematic drawings to provide consultant approved quantities to meet design intent.

All components that comprise the various systems shall be UL listed where a UL listing exists for that component or system.

Equipment provided by this contractor shall be fully coordinated with all other equipment required for complete system function.  This includes power, cooling, cabling, mounting equipment and locations, and controls.

SUBSTITUTIONS

Consideration for substitutions during the construction phase shall be allowed in light of a significant gain or advantage in quality of product or considerable cost savings to the Owner.  It is the contractor’s responsibility to obtain approval on all substitutions prior to installation. FAILURE TO OBTAIN APPROVAL FOR SUBSTITUTIONS SHALL BIND THE CONTRACTOR TO PROVIDING THE SPECIFIED EQUIPMENT WITHOUT REQUEST FOR ADDITIONAL PAYMENT. Contractors request for approval shall include the reason for requesting the substitution along with any relevant product data.

Requests for substitutions must be made at least 20 days prior to intended installation.

EQUIPMENT SPECIFICATIONS

Equipment/parts list provided as reference and/or example of quality and functionality.  Items on list may NOT be modified without prior Owner or Engineer approval.  It is the intent that the mentioned products herein be utilized, but if alternates are available to provide the same features and functions, the equipment noted here may be considered a basis of design and comparison for substitutes that can be demonstrated to be of equal quality and function.

Audio Digigital signal processor

Manufacturer: Biamp

Model: AudiaFLEX CM chasis with CobraNet Module, 2RU

Mic/Line input card

      - Biamp-IP-2

      - 2-channel input

Mic/Line output card

      - Biamp-OP-2E

      - 2-channel output card

Control (Processor) system

Manufacturer: Crestron CP3

      - 3 Series or better

Touch screen control

Manufacturer: Crestron

      - Crestron TSW-1050-SW-B-S

      - 10.1” touch screen, black, smooth

      - Custom rack panel with cutout for TSW

      - Programming

Customer must own original source code upon completion

Preview of touch panel layout must be provided to customer for approval prior to loading

Ethernet switch

Contractor shall coordinate with owner for access to their Ethernet switches in order to provide network connectivity to all areas.

Contractor shall provide Cat 6 network patch cords as required to connect to owner’s network devices.

Power over ethernet (Poe) injector

Manufacturer: Araknis

      - AN-ACC-INJ-30W-100

      - Network accessory Gigabit PoE+ injector

CABLING

All applicable provisions of the NEC and local codes shall apply.

Where AV signals are transported with Category 6 cable, use exact cable recommended by equipment manufacturer.  If manufacturer does not have a recommendation, use shielded Category 6 with shielded connectors.

All cabling shall be in accordance with manufacturer's recommendations. If the manufacturers recommended cabling for equipment proposed as equivalent in quality and performance cannot be accommodated in the conduit indicated in the contract documents, without exceeding normal fill or code requirements, the contractor shall furnish and install the additional required conduit without cost to the Owner.

All systems wiring shall be color coded with labeling and coding as submitted and approved by shop drawing.

Cabling shall be continuous and shall not be spliced between equipment. Color coding and tagging shall be maintained throughout the system at all accessible locations to the cabling.

Provide new floor box device plates as required for XLR connections in floor boxes if alternate is accepted.

AV system cabling is divided into classes that may not be intermixed within a conduit or raceway. Conduits for different AV cabling classifications must maintain minimum separations from each other and from other services.  In certain cases, AV system cabling of different classes may pass through or terminate in a common enclosure provided that proper separation is maintained within the enclosure. AV system cabling may not be intermixed with AC wiring within a conduit, raceway or enclosure. AV system cabling may not be intermixed with wiring related to any other trades or discipline including but not limited to; fire protection, HVAC, CATV, alarm, intercom, master clock, access control or other similar systems within a conduit, raceway or enclosure.

Wiring classifications, type and minimum separations are as follows.  Not all cabling will apply to all projects.  They are noted here as a reference.

All voice/data/audio/visual cabling run free air (not in conduits) must meet or exceed NEC requirements and be suitable for the environment for which it is installed (plenum rated).

Microphone level:

22 Ga. Stranded copper (7x30), insulated conductors, shielded twisted pair, bonded foil shield 100% coverage and 22 A WG stranded tinned copper drain wire. ASTM tinned copper conductor 22 A WG. Polypropylene insulation thickness: 008 (.20mm) Overall bonded @ shielded with aluminum foil. Overall 75° C PVC jacket Nom. jacket thickness .020" (.51 mm) Nominal O.D.  135" (3.43 nun) Electrical Characteristics: Nominal capacitance: 34 pf/ft.> 67 pf/m. Nom. D.C.R. @ 20°C: 17 Oil 000 ft. Nom. Velocity of Prop. : 66%

Maintain minimum 6" separation from conduits containing other low voltage services. Maintain minimum 12" separation from long parallel conduit runs containing AC voltages below 250 volts. Maintain minimum 24" separation from long parallel conduit runs containing AC voltages greater than 250 volts.

Acceptable: West Penn 454 or approved equal by Canare

Line level Audio:

22 AWG Stranded copper (7x30), insulated conductors, shielded twisted pair, bonded foil shield 100% coverage and 22 AWG stranded tinned copper drain wire, ASTM tinned copper conductor 22 AWG, Polypropylene insulation thickness: 008 (,20mm) Overall bonded @ shielded with aluminum foil. Overall 75·C PVC jacket Nom, jacket thickness, 020" (.5 I nun) Nominal OD, 135" (3.43 mm).

Electrical Characteristics: Nominal capacitance: 34 pf/ft.* 67 pf/m. Nom. D.C.R. @ 20·C: 17 n/1000 ft. Nom. Velocity of Prop. 66%

Maintain minimum 6" separation from conduits containing other low voltage services. Maintain minimum 12" separation from conduits containing AC voltages below 250 volts. Maintain minimum 24" separation from conduits containing AC voltages greater than 250 volts.

Acceptable: West Penn 454 or approved equal by Canare

Speaker level Audio:

Insulated copper, twisted pair or THHN sized per drawings. # t0 THHN or twisted pair for sub-woofers, #12 twisted pair equal to West Penn 227 for all direct coupled loudspeakers, # 16 twisted pair equal to West Peru1 225 for 70 volt circuits.

Maintain minimum 6" separation from conduits containing other low voltage services, Maintain minimum 6" separation from conduits containing AC voltages below 250 volts. Maintain minimum 12" separation from conduits containing AC voltages greater than 250 volts.

Acceptable manufactures: Belden, Covid, Extron, West Penn, Whirlwind, Canare

AV control system:

18 Ga. Stranded copper minimum, or greater as required for distance and current draw, Insulated conductors, quantity and shielding as required per equipment manufacturer. Maintain minimum 6" separation from conduits containing other low voltage services, Maintain minimum 12" separation from conduits containing AC voltages below 250 volts. Maintain minimum 24" separation from conduits containing AC voltages greater than 250 volts.

Acceptable manufactures: Liberty AMX AX Link or equal

Cat 6 Shielded Cable

Shall meet ANSI/TIA/EIA-568-A Category 6 standards

HDMI Cable

Standard 19-pin, type A, category 2 certified, 340MHz

CONDUIT REQUIREMENTS

    - It is assumed no conduit is required on this project.  All cable runs are made within AV racks.

– EXECUTION

GENERAL

Verify dimensions and conditions at the project site. Submit any conflicts in a timely manner for resolution.  AV contractor shall coordinate their efforts with other trades or existing utilities to ensure timely completion of their work and to avoid conflicts over scheduling, access and locations of their work.  It is currently anticipated that only AV work will be required and there will be no other trades other than county maintenance personnel.

Furnish all mounting brackets, raceways, sleeves, rack rails, termination plugs, jacks, faceplate mounting hardware, and other unique components as necessary to securely mount equipment and panels.

Furnish all required equipment whether or not specifically mentioned in these specifications or all the drawings.  Such devices shall include but not be limited to hardware, fasteners, rack screws, rack brackets, power supplies, fan guards, impedance matching devices, transformers, line pads, line amplifiers, relay and LED power supplies, and other devices as necessary to interface, control, or balance the AV systems.  Facilitate the integration of other room systems including lighting control systems and existing overhead page system.

Contractor shall determine the "installed" price for the AV system in each sub system. The costs are to include material, labor, installation, testing, documentation, commissioning, manuals, training, warranty; and the AV proportion of the Schedule of Values consisting of general conditions, bond, mobilization, record drawings, punch list, cleanup, and demobilization.

Protect all installed products until completion of project.  Touch up, repair or replace damaged products before substantial completion.

Material quantities

Quantities of  required equipment may be indicated on project documents based upon observed existing conditions.  For instance, the quantity of certain input and output devices may be correlated to the quantity of existing inputs and outputs currently in use.

While such quantities may be indicated on project documents the contractor remains responsible to provide all required input and output devices, ports or cards that are required to fully connect to the existing systems.

Auido Digital Signal processor

Provide DSP in existing AV rack for each AV room or rack as indicated on project documents

      - Provide new DSP to accommodate all required connections per project documents

      - Provide all input and output cards as required to connect to existing equipment

      - Provide one additional input port and one additional output port beyond what is currently required to connect to existing equipment.  If cards only come in two ports, then provide two additional ports if there are no spares remaining after all existing equipment has been connected.

      - Provide all cables, connections, programming and other equipment and labor for complete function including routing, balancing and equalizing.

      - Test operation and complete functioning

      - Coordinate with owner to provide a separate VLAN on their Ethernet network for CobraNet and control.

Control (Processor) system

Provide control processor in each existing AV rack

Connect to DSP and to owner’s network as required for complete function

Install all software and provide all required programming to permit any input from any location to be routed to any output at any location by means of touch screen control

Coordinate with owner to provide a separate VLAN on their Ethernet network for CobraNet and control.

Touch screen control

Consult closely with owner to relocate or adjust existing equipment to create  room for new touch panel display within racks

Provide touch screen control panel in AV racks

Provide custom rack panel with cutout as required

Provide patch cord to PoE injector

Provide all programming required for audio routing as described above

Consult closely with owner for touch screen appearance, buttons, functions

Provide a submittal to engineer/owner indicating proposed screen shots for each audio control screen, on/off and other functions

Coordinate with owner for access to their Ethernet network.

Connect all existing venues and outlying buildings to the CobraNet system per owner direction.

Provide programming as required to include all venues and outlying buildings as directed by owner.

Power over ethernet (Poe) injector

Provide PoE injector for touch screen

Provide patch cords as required to connect to touch screen and user’s network

Connect to power source as required

Test, balancing, tuning

Provide minimum 30 hours of testing, balancing and tuning to include all venues, all meeting rooms

Use equalizer, analyzer, sound meter and other equipment as required to perform tuning of system for optimal performance in each venue

Adjust output so that each venue’s sound level meets or exceeds the baseline measurements using default settings.

1. Contractor shall first sample sound levels in 3 customer specified venues for each AV room to obtain a current, existing baseline SPL levels.

2. Contractor shall meet or exceed the baseline for every venue after installation of new equipment.

3. Baseline measurements shall be made using a pink noise generator and SLP meter at 6’ AFF using current maximum level setting (without distortion and or clipping).  SPL meter weighting used during test is to also be recorded and the same weighting used for all tests.Test with all mic inputs

Eliminate feedback

Invite owner for final walk-through to confirm tuning, balancing and audio levels meet with owner’s approval.

Obtain owner sign-off after walk-through to confirm owner’s acceptance of complete installation.

WIRING

All cables and wiring are to be logically, legibly and permanently labeled for easy identification. Each wire shall be permanently marked with a number at each end. This applies to wire within a rack assembly as well as wire running in conduit. Labels on cables to be adhesive strip type covered with clear heat-shrink tubing. Factory stamped heat shrink tubing may be used in lieu of the adhesive strip style label. Hand-written or self-laminating type labels are not acceptable.

Wiring designations shall be an alpha-numeric code that is unique for each cable. Locate the cable designation at the start and end of each cable run and within 2 inches of the point of termination or connection. Label must be printed in three lines so that the designator is visible from all angles. For cable runs that have intermediate splice points, the cable shall have the same designation throughout with and additional suffix to indicate each segment of the run. Actual cable designation assignments shall be determined by the installing contractor. The overall system of wire designators shall be uniform throughout the entire project from sub-system to sub-system.

Provide adhesive labels on the rear of equipment where cables attach to indicate the designation of the cable connected at that point.

Exposed cables shall be enclosed with surface raceway.

All screw on terminals shall have crimp-on terminal lugs.

Wire ends and shield drain wires shall be covered with shrink tubing.

All cables in racks and custom panels shall be harnessed with suitable nylon tie wraps in a vertical and horizontal configuration. Cables that break out from harnesses for connection shall be provided with an adequate amount of slack cable for a service loop to provide access to equipment for servicing and adjustment.

EQUIPMENT GROUNDING

Bond all metallic parts to approved equipment ground.

WORK IN OTHER SECTIONS

The division of responsibility regarding work to be done by the AV contractor shall be in accordance with the following:

The following work shall be the sole responsibility of the AV contractor:

      - Furnish and install all equipment, panels, and devices associated with the AV systems as indicated on project documents

      - Termination of all AV systems wiring:  Coordination with owner for AC 120 volt power and wiring within AV systems cabinet and/or user locations

      - Preparation of AV shop drawings, maintenance manuals, wiring diagrams and other submittals required by the individual AV system specification sections

      - Tests, balancing, trouble shooting, adjustments and other similar work as may be required to insure complete operating AV systems

      - All AV training sessions required by these specifications

      - Any and all warranty work associated with the building audio visual systems

      - Any other work associated with the AV systems that due to its technical nature should logically be performed by the AV contractor.

      - Absence of shorts between conductors

      - Absence of shorts between conductors and conduit

      - Specified bandwidth is maintained

      - Impedance is maintained

Documentation shall include a chart listing applicable data.

Create, then provide Verification Checklist for each space or system.  Checklist should include all equipment indicated on project documents and may also include important items from this execution specification.  Where no coax is utilized, some sweep tests may not be required.

Verify that all loudspeakers and mountings are free of buzzes and rattles when swept with sign wave tones throughout its rated bandwidth at normal levels.

Verify that correct polarity is maintained throughout the entire signal path.

Verify that all equipment and systems are operating to manufactures specifications.

Verify that audio systems are free of humming, buzzing, feedback, interference, spurious oscillations, digital artifacts or extraneous noises of any kind.

Verify uniformity of sound coverage throughout intended coverage area.  Contractor shall invite owner to attend testing sessions.  Contractor to adjust sound levels in every room to meet owner's expectations.

Verify with consultant measurement locations, conditions and measurement criteria.

Verify that all equipment is operating correctly and is operating to manufacturers specifications.

Perform sound system rough equalization, cross over and delay settings and final sound system settings. Perform all video system set up and calibration.

Verify proper operation of all controls.

Verify each installed data network cable or fiber optic cable conforms to TIA/EIA performance standards.

Submit three (3) copies of a Systems Checklist or written report detailing the results of Initial Adjustments and Verification tests including all relevant drawings, charts, test instrument data and photographs. This report shall be complete and submitted to the engineer for review a maximum of five (5) days after substantial completion. With this report, submit written certification that the installation conforms to the requirements stated herein, is complete in all respects, and is ready for owner engineer final inspection and/or owner move-in.

Project is not complete until a Systems Checklist has been submitted.  The Checklist shall identify all systems and major components required for system function.  The Systems Checklist shall be filled out by contractor during systems operational testing prior to informing AE or Owner that system is complete.

Systems Checklist shall be presented to the Engineer prior to final punch list.

At Engineer request, Contractor shall be present during punch list to demonstrate function of all systems to Engineer and/or Owner.

Provide Systems Checklist per section 27 05 00.  Below is only an example of possible Systems Checklist.  Modify as required for audio system verification.  Contractor shall augment or add columns and rows to this list according to what makes sense for each major system component.  The point is to verify that all equipment has been turned on, functions as desired or has been adjusted to meet requirements.  Lack of such a check list indicates to Engineer and owner that systems have not been verified as functioning by contractor.

| Item Description | Observed Operation | dB SPL at 72” AFF | Adjustments Needed | Limitations | Date Item Verified/Initials |
| --- | --- | --- | --- | --- | --- |
| Exhibit Hall X | Yes |  |  |  | 9/10/15 R.K. |
| Meeting Room X | Yes |  |  |  | 9/10/15 R.K. |
| Meeting Room Y | Yes |  |  |  | 9/10/15 R.K. |
| Atrium | Yes |  |  |  | 9/10/15 R.K. |

TRAINING

Demonstrate to Engineer and/or owner that all individual components and all integrated systems function according to the design intent of the project documents and according to manufacturer’s recommendations.

Before scheduling such a demonstration it is the responsibility of the contractor to assure that all components and systems are functioning properly.

The AV contractor shall conduct group and/or individual training sessions, as requested by the Owner, for the proper operation and maintenance of the complete system.

Training shall provide a total of at least four hours of instruction at the site encompassing each system installed and shall orient responsible personnel to a level satisfactory to the Owner and Consultant. Training times shall be arranged with the Owner. The training shall include the facilities electrician or other designated personnel.  Training shall not take place until all systems are 100% operational and Systems Checklist has been completed.

Training shall be sufficient to permit Owner to fully understand and operate all systems without assistance.

WARRANTY

See General Conditions.

Warranty period shall be a minimum of one year. Warranty period shall commence at substantial completion or first beneficial use of system by owner, whichever comes first. During the warranty period, AV contractor shall furnish on site diagnostic and repair service to installed AV systems free of charge to owner. Contractor shall respond to service requests within 24 hours. Contractor shall provide on-site diagnostic and repair service within two business days of trouble report. Contractor shall make available after hours or weekend service at a premium rate not to exceed 1.5 times normal hourly rates minus normal hourly rates.

During the warranty period, the AV contractor shall provide for three service and maintenance calls by technically qualified personnel without additional charge. Calls shall be at least two hours at the site and shall be pre-arranged at least two weeks prior with the Owner

These service and maintenance calls shall be in addition to any warranty required service calls and shall commence 4 months after the date of final acceptance by the Owner.

All tests, adjustments, or replacements shall be made in the presence of Owner's technician, or other person designated by the Owner's superintendent. Upon completion of each call a report will be provided to clearly indicate any replacements or adjustments and any evidence of tampering.

The price for this warranty shall be included in the base bid price and shall not be superseded by any other long-term maintenance contract.  This warranty is meant to cover the current installation on the current contract and to coincide with the manufacturer’s one year equipment warranties.

If equipment installed under this contract fails within the first year, the contractor shall arrange for new equipment to be provided by the manufacturer at no cost to the owner and the contractor shall install that equipment at no cost to the owner.  The price for this labor should be included in the base bid.

This requirement is not meant to hold contractor responsible for failed equipment or installation after manufacturers’ warranties have expired.  See previous section of this specification for additional warranty after expiration of manufacturers’ warranties.

END OF SECTION

APPENDIX 2

Section 27 05 00

Common work results FOR COMMUNICATIONS SYSTEMS

- – GENERAL

  - SCOPE OF WORK

    - Base Bid:  It is the intent of these specifications to provide complete and workable telecommunications/audio systems – including all parts lists, operating instructions and wiring diagrams, as shown on the accompanying plans and as specified herein except such parts as are specifically exempted herein.  Provide all necessary supervision, coordination, labor, materials, equipment, fixtures, drayage, hoisting, tools, transportation, plant services and facilities, machinery and connections to utilities for the installation of complete and operable telecommunications systems.  If details or special conditions are required in addition to those shown on drawings, provide all material and equipment usually furnished with such systems or required to complete their installation, whether noted in plans and specification or not.

    - Materials and labor shall be new (unless noted otherwise), first class and workmanlike and shall be subject at all times to the A/E’s inspections, tests and approval from the commencement until the acceptance of the completed work.

    - The layout shown on the drawings is necessarily diagrammatic but shall be followed as closely as other work will permit.  The drawings provide design intent.  The Contractor shall verify all dimensions at the site and be responsible for their accuracy.

    - In the event of any inconsistencies between the specifications, drawings, contract documents, applicable laws, statutes, ordinances, building codes, rules and regulations, the contractor shall provide the better quality or greater quantity of work and comply with or conform its work to the most stringent legal or contractual requirements.

    - Changes from these drawings required to make this work conform to the building construction shall be made only with prior written approval of the Architect/Engineer.  All proposed changes shall be shown on shop drawings.  All measurements shall be verified by actual observation and all work shall fit in place meeting the approval of the Architect/Engineer.

    - Equipment Specification may not deal individually with minute items required, such as, components, parts, controls, and devices which may be required to produce the equipment performance specified or as required to meet the equipment warranties.  Where such items are required to make the system operational, they shall be included by the supplier of the equipment at no additional cost, whether or not specifically called for.

    - Equipment, materials and accessories for communications systems as shown and noted on the drawings including but not limited to the following:

      - Maintaining of all communications and other low voltage connections outside of or passing through the work area to other areas.

      - New Electronic audio equipment, patch cables, programming

      - New wiring devices, jacks and cover plates.

      - Complete testing, certification and creation of as-builts for all locations.

  - SECTION INCLUDES

    - This section includes information common to two or more technical communications specification sections or items that are of a general nature, not conveniently fitting into other technical sections.

- Submittals

- Construction Verification Checklists

- Functional Performance Tests

- Reference Standards

- Quality Assurance

- Guarantee

- Work By Owner

- Operation And Maintenance Instructions

- Record Documents

- Continuity Of Existing Services

- Protection Of Finished Surfaces

- Regulatory Requirements

- Certificates And Inspections

- Coordination

- Sleeves And Openings

- Omissions

- Definitions

- Project/Site Conditions

- Salvage Materials

- Performance Testing

- Description

- Dimensions And Defined Locations

- Training

- Identification

- Demolition

- Building Access

- Equipment Access

- Housekeeping And Clean Up

- Cable Installation

- Testing

- Systems Checklist

  - RELATED WORK

    - Applicable provisions of Division 1 govern work under this section.

    - This section is applies to all Division 27 sections.

    - Section 27 40 00 – Audio-Visual Systems

    - This work is also subject to all requirements of NEC and FCC wherever applicable to work under this section.

  - SUBMITTALS

    - Submit shop drawings for equipment under each section per requirements listed in that section.

    - Submit for all equipment and systems as indicated in the respective specification sections, marking each submittal with that specification section number.  Mark general catalog sheets and drawings to indicate specific items being submitted and proper identification of equipment by name and/or number, as indicated in the contract documents.  Failure to do this may result in the submittal(s) being returned to the Contractor for correction and resubmission.  Do not submit hard copies of web pages.  Failing to follow these instructions does not relieve the Contractor from the requirement of meeting the project schedule.

    - On request from the A/E, the successful bidder shall furnish additional drawings, illustrations, catalog data, performance characteristics, etc.

    - Submittals shall be grouped to include complete submittals of related systems, products, and accessories in a single submittal.  Mark dimensions and values in units to match those specified.  Include wiring diagrams of electrically powered equipment.

    - The submittals must be approved before fabrication is authorized.

    - Provide electronic copies of all submittals for review.

    - Provide one-line drawings (or modify bid documents) to reflect actual installation plans and equipment.

    - Submit sample of construction verification checklist and sample of functional performance tests, forms, or criteria.

  - CONSTRUCTION VERIFICATION CHECKLISTS

    - Contractor is responsible for utilizing the construction verification checklists recommended under these specifications.

  - FUNCTIONAL PERFORMANCE TESTS

    - Contractor is responsible for utilizing functional performance test procedures to verify the proper function of all equipment.

  - REFERENCE STANDARDS

    - Abbreviations of standards organizations referenced in this and other sections are as follows:

Edit this list to agree with the specification sections that are actually used.

ANSI	American National Standards Institute

ASTM	American Society for Testing and Materials

EPA	Environmental Protection Agency

ETL	Electrical Testing Laboratories, Inc.

IEEE	Institute of Electrical and Electronics Engineers

IES	Illuminating Engineering Society

ISA	Instrument Society of America

NBS	National Bureau of Standards

NEC	National Electric Code

NEMA	National Electrical Manufacturers Association

NESC	National Electrical Safety Code

NFPA	National Fire Protection Association

UL	Underwriters Laboratories Inc.

  - QUALITY ASSURANCE

    - Substitution of Materials:

If the Contractor wishes to submit an alternate to the named manufacturers for any equipment, he may submit a voluntary alternative minimum 7 days prior to bid, stating the manufacturer’s name, model number, written, detailed product data.

Where materials or equipment are specified by name the proposed material or equipment must be identical to the specified material or equipment in all characteristics of quality, function and serviceability, regardless of application in the Project and, in addition, when the Architect deems that aesthetic significance is important, the equal material or equipment must be identical in all characteristics of visual appearance, design, color and texture.  Any proposed equal shall be submitted to Architect/Engineer for prior approval, which Architect/Engineer may approve or disapprove in its sole discretion.  Work performed or constructed with unapproved equals is at Contractor’s risk and any required correction of work incorporating unapproved equals shall be at Contractor’s sole cost and expense.

In all instances, Contractor shall assume full responsibility for proof of equality of the statute to the equipment hereinafter specified.  All data and information necessary for proof of equality, function and space requirements shall be prepared and accompany the submittal of the substitution to the Architect/Engineer.  Approval by the Architect/Engineer of equipment other than the specified does NOT relieve Contractor of this responsibility.

    - All products and materials used are to be new, undamaged, clean and in good condition. Existing products and materials are not to be reused unless specifically indicated.

    - Where equipment or accessories are used which differ in arrangement, configuration, dimensions, ratings, or engineering parameters from those indicated on the contract documents, the contractor is responsible for all costs involved in integrating the equipment or accessories into the system, including, but not limited to, coordination with other trades and any required changes by other trades and for obtaining the intended performance from the system into which these items are placed.

    - General:

      - Audio Visual, Cable and Equipment Manufacturer(s) shall be a company specializing in communications cable, accessories and/or equipment with minimum of 5 years documented experience in producing cable, accessories and/or equipment similar to those specified herein.

    - Contractor Qualifications:

      - Qualified personnel utilizing state-of-the-art equipment and techniques shall complete all cable and equipment installation and termination.

      - Contractor shall have been in this business for minimum of 5 years and completed 4 projects of magnitude specified in the following sections.

      - See Section 27 40 00 for additional requirements.

  - GUARANTEE

    - Contractor shall meet the following requirements.

    - In entering into a contract covering this work, the contractor accepts the specifications and guarantees that the work will be carried out in accordance with the requirements of this specification or such modifications as may be made under the contract documents.

    - Contractor further guarantees that the workmanship and material will be of the best procurable and that none but experienced workmen familiar with each particular class of work will be employed.

    - Contractor further guarantees to replace and make good at his own expense, including travel time, all defects, which may develop within 1 year after final payment and acceptance by the Architect/Engineer, due to faulty workmanship or material, upon, receipt of written notification from the Owner.

  - WORK BY OWNER

    - Owner will provide assistance as required for access to facility, advice regarding features and functions and touch panel appearance preferences

    - Owner will provide electrical power and conduit as required

    - Owner will provide Ethernet network switches to access common network for audio signal routing

    - Owner will test all speakers for function

    - Owner will provide any required network tie cables between AV rooms or other buildings on site for network connection

Explain what systems or subsystems have been provided or sized for future expansion and what the Contractor must do to maintain these provisions.  This article is not needed if equipment is the only item that has been sized for the future, if the future capacity of that equipment is indicated on schedules, and if no other work is required of the contractor for this future provision.

  - OPERATION AND MAINTENANCE instructions

    - Supply the following additional documentation:

      - Copies of all approved submittals along with approval letters

      - Certificates of performance, employee attainments, registrations (see section 27 40 00)

      - Warranties

      - Operation manual documents to assist the Owner to maintain all systems

      - Records of test performed to certify compliance with system and manufacturer requirements

      - Full equipment cut sheets including brands, makes, models, supplier (retailer) and manufacturer information (name, phone, e-mail, website, contact name), one-line diagrams, cable connections, system architecture

      - Contractor information (name, phone, e-mail, website, contact name)

      - Systems checklist (refer to Part 3 below)

  - Record documents

    - In addition to the general content specified under section 27 40 00, follow the following procedures.

      - During the progress of the work, Contractor shall maintain a current (daily) record set of the drawings and specifications, indicating thereon all work installed at variance with such Contract Documents including, without limitation, work covered by Addenda, Field Work Orders, Change Orders and Engineers additional instructions, interpretations and clarification.  All changes or deviations from the original layout of the work and all critical dimensions of buried or concealed work shall be recorded.  It shall be Contractor’s responsibility to assure that said record sets are complete, accurate and up-to-date, Engineer shall have the right to inspect and review such record sets.

      - At the completion of the work, Contractor shall indicated on record sets all record changes and such additional details necessary or appropriate to provide a complete reference document for use by Engineer.  If variations and details cannot be shown clearly thereon, the Contractor shall prepare supplemental drawings adequate to impart the information.  The foregoing drawings collectively shall constitute the “Record” drawings for the work.

      - All indication on “Record” drawings shall be executed in a legible manner at Contractor’s cost, using methods and legend presentations compatible with the overall scheme of the record drawings with respect to scale, drawing sheet sizes and sequential indexing.  All changes shall be marked clearly in red and clouded.

      - Engineer may review Contractor’s “Record” drawings and notify Contractor of observed discrepancies or deviations.  Contractor shall promptly correct discrepancies, deviations or illegible markups at Contractor’s expense and resubmit revised drawings for Engineer reviewSelect one of the following two paragraphs depending on who is responsible for final electronic record drawings.  This may be decided in our contract with the client.

      - Contractor shall provide final electronic record drawings to the Owner through the Engineer.

      - Engineer will provide final electronic record drawings to the Owner based on Contractor’s markups.

  - CONTINUITY OF EXISTING SERVICES

Consider what level of down time is acceptable.  Discuss with the Owner.  If work is required on weekends, nights or holidays, this must be indicated in the specifications and/or on the drawings.  Add specifics including location, which service, hours when work is to be scheduled, required sequencing with other work, etc.  Choose either the following paragraph or next 3 paragraphs.

    - Do not interrupt or change existing services without prior written approval from the Owner's Project Representative.  When interruption is required, coordinate scheduling of down-time with the Owner to minimize disruption to his activities.  Unless specifically stated, all work involved in interrupting or changing existing services is to be done during normal working hours.

    - Contractor shall thoroughly familiarize himself with existing systems which will affect and be affected by relocation of existing equipment and installation of new lines and equipment.  They shall plan installation of their work so that interruptions of services to any building or portion thereof will be a minimum and such interruptions shall occur only when system is not required, if possible.  If not possible, each Contractor shall insure the operation of services by whatever means possible, such as, installing bypasses, capping of services or providing temporary service.  Each interruption shall be for as short a duration as possible.Bypasses or temporary services may add cost.  If required, show bypasses or temporary services on phasing plans or floor plans.

    - No extra costs will be paid to the Contractor for such outages which must occur outside of regular weekly working hours.

    - This Contractor shall restore any circuit interruption as a result of this work to proper operation as soon as possible.  Note that institutional operations are on a seven day week schedule.

    - Contractor shall coordinate with Owner for access to the various rooms which may be in use at various times.

  - PROTECTION OF FINISHED SURFACES

    - Refer to Division 1 for protection of finished services.

    - Furnish one can of touch-up paint for each different color factory finish furnished by the Contractor.  Deliver touch-up paint with other "loose and detachable parts" per Division 1.

  - regulatory requirements

    - Comply with requirements of Wisconsin Administrative Code and local Authority Having Jurisdiction (AHJ) regarding materials and installation.

  - CERTIFICATES AND INSPECTIONS

    - Obtain and pay for all required State or local installation inspections except those provided by the Architect/Engineer in accordance with State Code.  Deliver originals of these certificates to the Owner.  Include copies of the certificates in the Operating and Maintenance Instructions.

    - Coordinate and provide inspections as required by the Authority Having Jurisdiction over the site.

On projects involving the use of Federal funds, inset "and Federal" after "State" in the first line above.

  - COORDINATION

    - It shall be the responsibility of each Contractor to coordinate and consult with each other to determine space requirements and to determine that adequate space for servicing is provided for all equipment whether furnished by the Contractor or others.  The General Contractor shall have final decision on all space priority conflicts among Contractors.  All space priority conflicts shall be brought to the attention of the Architect/Engineer and Owner's Representative.

    - Contractor shall thoroughly familiarize himself with existing systems which will affect and be affected by relocation of existing equipment and installation of new lines and equipment.  They shall plan installation of their work so that interruptions of services to any building or portion thereof will be a minimum, and such interruptions shall occur only when system is not required, if possible.  If not possible, Contractor shall insure the operation of services by whatever means possible, such as, installing bypasses, capping of services, or providing temporary service.  Each interruption shall be for as short a duration as possible.

    - Any installed work that is not coordinated and interferes with another contractor’s work shall be removed or relocated at the installing contractor’s expense.The following paragraphs apply only to large or complex projects requiring coordination drawings.  It is also recommended that the designer coordinates with other designers.  It is assumed that the Ventilating/Mechanical Contractor will lead the process.  If there is no ductwork, then a different contractor should lead.  Coordinate specs with other designers.

  - OMISSIONS

    - No later than ten (10) days before bid opening, the Contractor shall call the attention of the A/E to any materials or apparatus the Contractor believes to be inadequate and to any necessary items of work omitted.

  - PROJECT/SITE CONDITIONS

List special or unusual project conditions affecting the Contractor's work.

    - Install Work in locations shown on Drawings, unless prevented by Project conditions.

    - Prepare drawings showing proposed rearrangement of Work to meet Project conditions, including changes to Work specified in other Sections.  Obtain permission of A/E before proceeding.

    - Tools, materials and equipment shall be confined to areas designated by the Owner’s project representative.

  - WORK SEQUENCE AND SCHEDULING

    - Install work in phases to accommodate Owner's occupancy requirements.  During the construction period coordinate schedule and operations with Owner's Construction Representatives.

  - SALVAGE MATERIALS

    - No materials removed from this project shall be reused (except as specifically noted below).  All materials removed shall become the property of and shall be disposed of by the Contractor.

  - PERFORMANCE TESTING

    - Each system included in project scope shall be tested to verify performance.

    - Systems that require a performance warranty (such as data cable) shall be tested to comply with manufacturer’s requirements in order to obtain the system warranty.

    - Some systems have specific testing procedures (fiber optic cable).

    - Systems not having specific testing criteria shall utilize the Systems Checklist described in Part 3 below.

  - DESCRIPTION

    - The project consists of augmenting an existing audio distribution system.

    - Equipment and cabling work occurs mostly within AV rooms and AV racks.

    - Testing, balancing and tuning of sound system will require contractor to visit, walk and survey multiple meeting rooms and other venues to assure audio levels, balance, coverage and lack of feedback.

    - Systems shall be delivered in complete functioning condition.

    - Coordinate with owner as required to obtain owner furnished items.

  - DIMENSIONS AND DEFINITE LOCATIONS

    - The Drawings depicting Work show approximate locations.  The exact location of equipment and devices shall be established in the field in accordance with instructions from the Owner.  Consideration shall be given to construction features, equipment of other trades, and requirements of the equipment proper.

    - The Contractor shall refer to Shop Drawings and submittal drawings for all equipment requiring electrical connections to verify rough-in and connection locations.

    - Unless specifically stated to the contrary, no Drawing by scale shall be used as a dimension to Work by.  Dimensions noted on the Drawings are subject, in each case, to measurements of adjacent or previously completed Work and all such measurements necessary shall be taken before undertaking any Work dependent upon them.

  - training

Delete the above line if no commissioning is provided on the project. Delete the lines below if commissioning is provided.

    - The contractor shall have the following responsibilities:

      - Provide a training plan sixty days before the planned training covering the following elements:

        - Equipment

        - Intended audience

        - Location of training

        - Objectives

        - Subjects covered (description, duration of discussion, special methods, etc.)

        - Duration of training on each subject

        - Instructor for each subject

        - Methods (classroom lecture, manufacturer’s quality video, site walk-through, actual operational demonstrations, written handouts, etc.).

      - Provide designated owner personnel with comprehensive orientation and training in the understanding of the systems and the operation and maintenance of each piece of equipment that makes up the system.

      - Training shall normally start with classroom sessions followed by hands-on demonstration/training on each piece of equipment.

      - During any demonstration, should the system fail to perform in accordance with the requirements of the O&M manual or sequence of operations, the system shall be repaired or adjusted as necessary and the demonstration repeated at another scheduled time, if necessary.

      - The appropriate trade or manufacturer's representative shall provide the instructions on each major piece of equipment. Practical building operating expertise as well as in-depth knowledge of all modes of operation of the specific piece of equipment are required.  More than one party may be required to execute the training.

      - The training sessions shall follow the outline in the table of contents of the operation and maintenance manual and illustrate whenever possible the use of the O&M manuals for reference.

      - Training shall include:

        - Use of the printed installation, operation and maintenance instruction material included in the O&M manuals.

        - A review of the written O&M instructions emphasizing safe and proper operating requirements, preventative maintenance, special tools needed and spare parts inventory suggestions.  The training shall include startup, operation in all modes possible, shutdown, seasonal changeover and any emergency procedures.

        - Discussion of relevant health and safety issues and concerns.

        - Discussion of warranties and guarantees.

        - Common troubleshooting problems and solutions.

        - Explanatory information included in the O&M manuals.

        - Discussion of any peculiarities of equipment installation or operation.

        - Classroom sessions shall include the use of overhead projections, slides, video/audio-taped material as might be appropriate.

        - Hands-on training shall include startup, operation in all modes possible, including manual, shut-down, alarms, power failure and any emergency procedures, and preventative maintenance for all pieces of equipment.

      - The contractor shall fully explain and demonstrate the operation, function and overrides of any local packaged controls not controlled by the central control system.

    - Provide a minimum of 4 hours of instruction.  Engineer to provide number of hours based on owner’s staff and the size of the project. This training is for general operation, equipment training is included in each equipment specification.Return to site if 2 sessions of 2 hours each are required.

    - Provide additional training as specified in other specification sections for specific equipment.

The requirement for recording training sessions may be deleted on some projects but not the requirement for the training itself.

- – PRODUCTS

Coordinate this item with the Architect.  Not only are aesthetic parameters involved, but also the Architect must indicate in the General specifications that the General Contractor must install a certain number of these openings so that the costs will be included in the bid.

  - Identification

    - All new cables shall be identified by cable type, pair count, function and/or destination to assist owner with future identification.

- – EXECUTION

  - DEMOLITION

    - Perform all demolition as indicated on the drawings to accomplish new work.  Where demolition work is to be performed adjacent to existing work that remains in an occupied area coordinate work with the Owner to minimize disruption to the existing building occupants.

Where demolition work is extensive or complex, separate details or drawings are required [rather than notes on the construction drawings] to accurately illustrate the extent of the work.  Reproduction of photographs on the demolition drawings may be appropriate.  Do not specify demolition work "as required" - it does not give the Contractor sufficient information for proper bid preparation.  Identify each piece of equipment that is to be turned over to the Owner.

  - BUILDING ACCESS

    - Arrange for the necessary openings in the building to allow for admittance of all apparatus.  When the building access was not previously arranged and must be provided by this contractor, restore any opening to its original condition after the apparatus has been brought into the building.

    - Access will need to be carefully coordinated with the Owner.  This could mean a delay in certain operations.  Contractor shall account for such delays and coordination in their bid.  In exchange for possible delays, the Owner agrees not to hold the contractor to an unreasonably short schedule.

  - EQUIPMENT ACCESS

    - Install all equipment and accessories to permit access to equipment for maintenance.

  - COORDINATION

    - The Contractor shall coordinate with owner regarding scheduling, removal of existing equipment, placement of new equipment in AV racks, look, feel and layout of touch panel display.

Modify the paragraph above to suit the project. Include a list of spaces where this paragraph is applicable either in the specification or on the drawings.

  - HOUSEKEEPING AND CLEAN UP

    - The Contractor shall clean up and remove from the premises, on a daily basis, all debris and rubbish resulting from its work and shall repair all damage to new and existing equipment resulting from its work.  When job is complete, this Contractor shall remove all tools, excess material and equipment, etc., from the site.

  - CABLE INSTALLATION

    - Furnish all required installation tools to facilitate cable pulling without damage to cable jacket.

    - Provide all patch cords for all equipment as required for complete function.

    - During pulling operation adequate number of workers shall be present to allow cable observation at all points of raceway entry and exit, as well as to feed cable and operate pulling machinery.

    - Pull cables in accordance with cable manufacturer's recommendations and ANSI/EEE C2 Standards.

    - Recommended pulling tensions and bending radii shall not be exceeded.

    - Any cables bent or kinked to radius less than recommended dimension are not allowed and shall be replaced at no expense to Owner.

    - Pull all cable by hand unless installation conditions require mechanical assistance.

    - Do not install audio cable near power cable.

    - Cable in MDF/TR shall be routed and supported utilizing "D-type" mounting rings, J-hooks and overhead cable runway.

    - Use of circular bridle rings made of round stock is not acceptable for cable support.  Any support device must have a flat bottom (such as j-hooks) to adequately support cable without deforming cable at point of support.

    - Avoid abrasion and other damage to cables during installation.  Any cable having visible abrasions that have worn through the outer sheath shall be replaced at contractor's expense, whether the cable passes the certification test, or not.

    - Provide plastic bushings on the end of every conduit or sleeve that is utilized for cable.  Use of conduits or sleeves WITHOUT the provision of plastic bushings to protect the end of the conduit may be cause for removal and replacement of all cables utilizing that conduit or sleeve.

    - Install cables splice-free unless otherwise specified.

    - Cabling shall be neatly laced, dressed and supported.

  - TESTING

    - Contractor shall:

      - Submit schedule for acceptance testing.  Representatives of Owner and/or Engineer may witness test procedures.

      - Notify Owner and Engineer a minimum of 2 days in advance to allow for such participation.

      - Conduct tests during course of construction when identifiable portion of installation is complete.  Alternatively, testing can be conducted after entire installation is complete if this does not delay the project schedule.

      - Describe test procedures prior to testing and submit sample test form to Engineer.  Submit 3 record copies, and one electronic copy in CSV format, of results of tests to Engineer for approval.

      - Alternatively, Contractor may submit proprietary electronic format test results, including software to access and print results.  Software shall be Windows™ compatible.

    - Testing shall be completed and accepted by Owner and Engineer before Owner furnished equipment and cross connects are installed.

    - Test results shall be provided to manufacturer in order to obtain complete cable system warranty within 30 days of project completion.  Provide original warranty certificate to owner and one copy to engineer.

    - Provide as-built jack plans and other as-built documentation as determined by field labeling or other changes to project documents.

    - The contractor is responsible to assure that all individual components and integrated systems (especially electronic systems) are fully functioning and in good working order before notifying Engineer or Owner for acceptance testing, inspection or final punch list completion.

  - SYSTEMS CHECKLIST

    - For all systems having an electronic equipment component (active electronics) a system checklist shall be developed and utilized by the contractor.

    - The systems checklist shall make note of all major electronic components and systems.

    - It shall utilize a simple method to make notations of the equipment, that they

      - Function individually as designed

      - Have been calibrated or adjusted

      - Function as an integrated system with other components

    - The checklist shall be utilized in the field by the contractor and filled out appropriately prior to contracting owner or engineer to witness tests, provide inspections or complete final punch list.

    - The checklist shall have a signature line for three entities: Contractor/supervisor, owner and engineer.

    - A completed, signed checklist (by Contractor) shall be presented to the engineer prior to performing the punch list and prior to final owner sign-off or project completion.

    - Examples of systems that might require a checklist: Access Control, Closed Circuit TV system (security cameras), Audio-Visual systems, Area of Rescue, Digital Signage, Nurse Call and other system that utilizes active electronics.

    - It is the responsibility of the Contractor, not the Engineer or Owner, to assure that all systems function according to the design intent of the project documents and according to all manufacturer’s recommendations prior to project completion.  The Systems Checklist shall be utilized by the Contractor and presented to the Engineer or Owner as verification that all systems have been tested, adjusted and are in good working order.

    - The Systems Checklist shall be included as part of the Operations and Maintenance manual to be submitted at project completion.

END OF SECTION